## Slide 1
1 · MAP THE SYSTEM
Async remote inference: the code
A guided route from your hardware intuition to a code review.
01
Map ownership
Who can change
which state?
02
Trace one
request
Capture → prediction
→ dispatch
03
Read execution
Timing, alignment and
blending
04
Review
boundaries
Invalidation, faults and
tests
Start with one chapter. Open code only when you want the next level of detail.
01
Notes: This companion describes the checked-out implementation on 30 September 2026. It includes the aligned playback-threshold correction and the later lifecycle changes. The earlier high-level deck is historical and describes that correction as planned.
Use the slide to form a mental model, then open the speaker notes for explanations, review questions, answers, and exact source excerpts. The companion HTML contains the interactive examples. Those examples change explanatory numbers only and never connect to a robot or server.
This is a learning guide, not a completed code review or a new specification. Hardware task/motion and focused lifecycle checks have operator-reported acceptance. Real language-model behavior and representative routed/WAN deployment remain separate work.
Review question: Which part should remain responsive while inference is running?
Answer: The local robot control loop. Network waits and policy execution live outside it.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/rollout/inference/remote.py:36 — RemoteInferenceEngine
src/lerobot/inference/execution.py:62 — ChunkRuntime
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/rollout/inference/remote.py:36 RemoteInferenceEngine
class RemoteInferenceEngine(InferenceEngine):
def __init__(
self,
client: RemoteClient,
config: RemoteInferenceConfig,
dataset_features: dict,
rename_map: dict[str, str],
robot_wrapper: ThreadSafeRobot,
task: str,
shutdown_event: Event | None = None,
) -> None:
super().__init__(task)
self.client = client
self.config = config
self._features = dataset_features
self._rename_map = rename_map
self._robot = robot_wrapper
self._global_shutdown = shutdown_event
self.runtime = ChunkRuntime(
mode=ExecutionMode(config.mode),
action_interval=client.capabilities.action_interval,
refill_seconds=config.refill_seconds,
max_observation_age_s=config.max_observation_age_s,
action_timeout_s=config.action_timeout_s,
startup_timeout_s=config.startup_timeout_s,
training_max_delay=client.capabilities.training_max_delay,
chunk_merge=config.chunk_merge,
blend_steps=config.blend_steps,
blend_weight=config.blend_weight,
blend_indices=tuple(
client.capabilities.action_feature.names.index(name) for name in config.blend_components
),
[Excerpt continues in the source file.]
src/lerobot/inference/execution.py:62 ChunkRuntime
class ChunkRuntime:
"""Capacity-one executor scheduling with per-action provenance and latched faults."""
def __init__(
self,
*,
mode: ExecutionMode,
action_interval: float,
refill_seconds: float,
max_observation_age_s: float,
action_timeout_s: float,
startup_timeout_s: float,
training_max_delay: int = 0,
chunk_merge: str = "append",
blend_steps: int = 0,
blend_weight: float = 0.5,
blend_indices: tuple[int, ...] = (),
clock: Callable[[], float] = time.monotonic,
) -> None:
"""Allocate one action queue and a bounded steady-state latency window."""
for value in (action_interval, max_observation_age_s, action_timeout_s, startup_timeout_s):
if not math.isfinite(value) or value <= 0:
raise ValueError("Execution intervals, ages and deadlines must be finite and positive")
if not math.isfinite(refill_seconds) or refill_seconds < 0:
raise ValueError("Refill playback threshold must be finite and nonnegative")
if chunk_merge not in {"append", "aligned"} or (
chunk_merge != "append" and mode is not ExecutionMode.CHUNK
):
raise ValueError("Aligned replacement is supported only for plain chunks")
if type(blend_steps) is not int or blend_steps < 0:
raise ValueError("Blend steps must be a nonnegative integer")
if not math.isfinite(blend_weight) or not 0 < blend_weight <= 1:
[Excerpt continues in the source file.]

## Slide 2
1 · MAP THE SYSTEM
Ownership follows the process boundary
The client owns motion permission. The server owns policy execution.
Robot client
Rollout strategy → RemoteInferenceEngine → ChunkRuntime → ActionQueue
Reads hardware, commits targets, interpolates, checks freshness and faults.
GPU server
PolicyServer → SessionWorker → PolicyRunner → policy + processors
Admits one session and serializes every operation that can mutate model state.
The shared runtime decides how to execute a result; Zenoh only carries the request and reply.
02
Notes: RemoteInferenceEngine coordinates a background network worker with the local control loop. ChunkRuntime owns scheduling, acceptance and dispatch permission. ActionQueue stores paired action representations with provenance and a commitment cursor.
SessionWorker owns exclusive policy/processor access. PolicyRunner knows canonical observations, preprocessing and model calls, but knows nothing about robot I/O or Zenoh. Shared execution concepts also support local RTC; synchronous select_action behavior remains its own path.
The review question is about authority: a network callback cannot send a motor command, and the control thread cannot reset the server policy while a forward call is in progress.
Review question: Where would a change to plain alignment belong?
Answer: In shared execution and its queue contract, with negotiation as needed—not in transport callbacks or a particular model forward method.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/rollout/inference/remote.py:374 — RemoteInferenceEngine._loop
src/lerobot/remote_inference/server.py:537 — SessionWorker._run
src/lerobot/inference/policy_runner.py:217 — PolicyRunner.predict
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/rollout/inference/remote.py:374 RemoteInferenceEngine._loop
def _loop(self) -> None:
try:
while not self._stop_event.is_set() and not self.failed:
# Control-thread dispatch only queues bounded diagnostics. Log
# from this worker so first-dispatch reporting adds no motor I/O.
with self.runtime.lock:
dispatch_events = list(self.runtime.dispatch_events)
self.runtime.dispatch_events.clear()
for event in dispatch_events:
self._event("first_dispatch", **event)
with self._lock:
control = self._control
observation = self._observation
hold_ready = self._hold_requested and self._hold_acknowledged
if control is not None:
# Language invalidation must be acknowledged by the motor thread
# before submitting any server-side generation operation.
if self._hold_requested and not hold_ready:
self._stop_event.wait(0.002)
continue
operation, generation = control
self.client.control(operation, generation)
with self._lock:
if self._control == control:
self._control = None
continue
if not self.runtime.active or observation is None:
self.runtime.check_deadlines()
self._stop_event.wait(0.002)
continue
if hold_ready:
with self._lock:
[Excerpt continues in the source file.]
src/lerobot/remote_inference/server.py:537 SessionWorker._run
def _run(self) -> None:
while not self._stopping.is_set():
try:
message, future, queued_at = self._commands.get(timeout=0.05)
except Empty:
continue
started = time.monotonic()
inference_operation = message.message_type in {
MessageType.OBSERVATION,
MessageType.LANGUAGE_REQUEST,
}
deadline = (
self.language_deadline_s
if message.message_type is MessageType.LANGUAGE_REQUEST
else self.action_deadline_s
)
try:
if inference_operation and started - queued_at > deadline:
response = message.error(ErrorCode.TIMEOUT, "Policy worker queue deadline exceeded")
if self._session is not None:
self._session.faulted = True
else:
response = self._execute(message)
except Exception as exc:
logger.exception(
"Policy worker failure instance=%s session=%s request=%s",
self.instance_id,
message.session_id,
message.request_id,
)
timed_out = time.monotonic() - queued_at > deadline
response = message.error(ErrorCode.TIMEOUT if timed_out else ErrorCode.EXECUTION, str(exc))
[Excerpt continues in the source file.]
src/lerobot/inference/policy_runner.py:217 PolicyRunner.predict
def predict(
self,
observation: ObservationSnapshot,
*,
mode: ExecutionMode = ExecutionMode.CHUNK,
inference_delay: int = 0,
model_continuation: torch.Tensor | None = None,
canonical_continuation: torch.Tensor | None = None,
provenance: ActionProvenance | None = None,
) -> ActionChunk:
"""Preprocess a fresh snapshot and return a validated canonical action chunk."""
mode = ExecutionMode(mode)
if mode not in self.capabilities.modes:
raise ValueError(f"Execution mode {mode.value!r} was not enabled by this deployment.")
started = time.perf_counter()
# Guided RTC locally enables autograd for its prefix correction. no_grad
# permits that override; inference_mode would suppress its gradient graph.
with torch.inference_mode(mode is not ExecutionMode.RTC_GUIDED), torch.no_grad():
prepared = self.preprocessor(self._batch(observation))
preprocessed_at = time.perf_counter()
kwargs: dict[str, Any] = {}
if mode != ExecutionMode.CHUNK:
prefix = self._prepare_continuation(model_continuation, canonical_continuation)
if inference_delay < 0:
raise ValueError("RTC delay must be nonnegative.")
if prefix is None and inference_delay:
raise ValueError("RTC delay requires a real continuation prefix.")
if mode == ExecutionMode.RTC_TRAINED:
available = 0 if model_continuation is None else len(model_continuation)
if inference_delay > min(
self.capabilities.training_max_delay, available, self.capabilities.rtc_horizon
):
[Excerpt continues in the source file.]

## Slide 3
1 · MAP THE SYSTEM
Two startup paths meet at admission
Weights stay on the server; the client builds a hardware contract.
Server startup
load_deployment → PolicyRunner → warmup → full reset → serve
Checkpoint + saved processors + effective settings become one advertised deployment.
Client startup
connect / describe → robot schema → admit → RemoteInferenceEngine
Camera names, joint order, semantics, action rate and mode must agree.
Successful warmup proves a callable path; it does not prove task performance.
03
Notes: load_deployment resolves the checkpoint (and PEFT base if configured), loads the policy and canonical processors, constructs the runner, computes artifact identity and warms the enabled paths. A full reset removes warmup state before readiness.
build_remote_rollout_context explicitly rejects a local policy, device or compilation setting. It discovers capabilities, connects hardware, collects the initial pose, aligns component order, applies the rename map and requests admission. Hardware connection and observation happen during setup; policy dispatch waits for compatibility and admission.
The artifact hash identifies loaded files and effective configuration. It is not a hash of all implementation code; package/revision information is logged separately.
Review question: Does “compatible before motion” mean the robot was never connected?
Answer: No. Setup connects and reads the robot to construct the contract. The guarantee concerns admitting remote policy execution and dispatching its actions.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/scripts/lerobot_policy_server.py:65 — load_deployment
src/lerobot/rollout/remote_context.py:51 — build_remote_rollout_context
src/lerobot/scripts/lerobot_rollout.py:227 — rollout
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/scripts/lerobot_policy_server.py:65 load_deployment
def load_deployment(cfg: ServerConfig) -> tuple[PolicyRunner, str]:
"""Resolve contents, load canonical processors and reset all warmed model paths."""
if cfg.action_feature is None:
raise ValueError("An explicit action feature is required")
path = resolve_artifact(cfg.model.repo_or_path, cfg.model.revision)
artifacts = {"checkpoint": path}
policy_cfg = PreTrainedConfig.from_pretrained(path)
policy_cfg.pretrained_path = path
policy_cfg.device = cfg.model.device
if hasattr(policy_cfg, "rtc_config"):
policy_cfg.rtc_config = cfg.execution.rtc
policy_class = get_policy_class(policy_cfg.type)
if policy_cfg.use_peft:
require_package("peft", extra="peft")
adapter = PeftConfig.from_pretrained(str(path))
base = resolve_artifact(adapter.base_model_name_or_path, adapter.revision)
artifacts["base"] = base
policy = policy_class.from_pretrained(base, config=policy_cfg)
policy = cast(PreTrainedPolicy, PeftModel.from_pretrained(policy, path, config=adapter))
else:
policy = policy_class.from_pretrained(path, config=policy_cfg)
policy.to(cfg.model.device).eval()
preprocessor, postprocessor = make_pre_post_processors(
policy_cfg=policy_cfg,
pretrained_path=path,
preprocessor_overrides={
"device_processor": {"device": cfg.model.device},
"rename_observations_processor": {"rename_map": {}},
},
)
runner = PolicyRunner(
policy,
[Excerpt continues in the source file.]
src/lerobot/rollout/remote_context.py:51 build_remote_rollout_context
def build_remote_rollout_context(
cfg: RolloutConfig,
shutdown_event: Event,
teleop_action_processor: RobotProcessorPipeline | None = None,
robot_action_processor: RobotProcessorPipeline | None = None,
robot_observation_processor: RobotProcessorPipeline | None = None,
) -> RolloutContext:
config = cfg.inference
if not isinstance(config, RemoteInferenceConfig) or cfg.robot is None:
raise ValueError("Remote rollout requires remote inference and robot configuration")
if cfg.policy is not None or cfg.device is not None or cfg.use_torch_compile:
raise ValueError("Remote rollout does not accept local policy/device/compile configuration")
client = RemoteClient.connect(config)
robot = None
teleop = None
try:
descriptor = client.descriptor
capabilities = descriptor["capabilities"]
expected = tuple(FeatureSpec(**feature) for feature in capabilities["features"])
action = FeatureSpec(**capabilities["action_feature"])
if not action.names:
raise ValueError("Remote rollout requires explicit ordered canonical action component names")
default_teleop, default_action, default_observation = make_default_processors()
teleop_action_processor = teleop_action_processor or default_teleop
robot_action_processor = robot_action_processor or default_action
robot_observation_processor = robot_observation_processor or default_observation
robot = make_robot_from_config(cfg.robot)
wrapper = ThreadSafeRobot(robot)
wrapper.configure_position_hold()
robot.connect()
[Excerpt continues in the source file.]
src/lerobot/scripts/lerobot_rollout.py:227 rollout
def rollout(cfg: RolloutConfig):
"""Main entry point for policy deployment."""
init_logging()
if cfg.display_data:
logger.info(
"Initializing %s visualization (ip=%s, port=%s)",
cfg.display_mode,
cfg.display_ip,
cfg.display_port,
)
init_visualization(cfg.display_mode, session_name="rollout", ip=cfg.display_ip, port=cfg.display_port)
signal_handler = ProcessSignalHandler(use_threads=True, display_pid=False)
shutdown_event = signal_handler.shutdown_event
if not isinstance(shutdown_event, threading.Event):
raise RuntimeError("ProcessSignalHandler(use_threads=True) must hand out a threading.Event")
if cfg.interactive:
# /reset and /stop end the control loop via the local flag; process signals still
# propagate through the parent event.
shutdown_event = LinkedEvent(shutdown_event)
logger.info("Building rollout context...")
ctx = build_rollout_context(cfg, shutdown_event)
strategy = create_strategy(cfg.strategy)
logger.info("Rollout strategy: %s", cfg.strategy.type)
logger.info(
"Robot: %s | FPS: %.0f | Duration: %s",
cfg.robot.type if cfg.robot else "?",
cfg.fps,
f"{cfg.duration}s" if cfg.duration > 0 else "infinite",
[Excerpt continues in the source file.]

## Slide 4
1 · MAP THE SYSTEM
The canonical data boundary
The wire carries named observations and canonical action targets.
Robot values
Robot observation
processor
+ ordered components
→
Snapshot / wire
RGB: HWC uint8
state: declared tensor
→
PolicyRunner
batch + saved
processors
predict_action_chunk
→
Robot command
canonical target
→ local action
processor
A six-element tensor is compatible only if its names, order and meaning also match.
04
Notes: FeatureSpec includes name, shape, dtype, kind, ordered component names and explicit semantic conventions. A shape match alone cannot tell degrees from normalized joint values or identify a swapped camera.
The client renames observation keys once. ObservationSnapshot copies arrays and marks them read-only because camera implementations may reuse buffers. On the server, _batch validates the exact negotiated schema, converts RGB HWC uint8 into batched CHW float values in [0,1], then invokes the saved policy preprocessor.
Canonical actions are policy postprocessor outputs before the local robot action processor. Do not confuse model-normalized actions, canonical targets, post-processor commands and measured positions. They are deliberately separate in the event log.
Review question: Why copy image arrays before asynchronous encoding?
Answer: The camera may overwrite a shared buffer while another thread is encoding it. The snapshot must own stable bytes.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/contracts.py:114 — ObservationSnapshot
src/lerobot/inference/policy_runner.py:195 — PolicyRunner._batch
src/lerobot/inference/contracts.py:34 — FeatureSpec
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/contracts.py:114 ObservationSnapshot
class ObservationSnapshot:
"""Owned immutable current observations with original capture provenance."""
features: Mapping[str, np.ndarray]
capture_time: float
task: str
task_version: int = 0
observation_id: str = ""
action_cursor: int | None = None
execution_generation: int | None = None
def __post_init__(self) -> None:
"""Copy camera buffers so asynchronous encoding sees a stable frame."""
if not math.isfinite(self.capture_time):
raise ValueError("Observation capture time must be finite.")
for anchor in (self.action_cursor, self.execution_generation):
if anchor is not None and (type(anchor) is not int or anchor < 0):
raise ValueError("Observation action anchors must be nonnegative integers.")
# Cameras commonly recycle their arrays. Own exactly one bounded request
# snapshot; copies remain read-only until the runner creates its batch.
owned: dict[str, np.ndarray] = {}
for name, value in self.features.items():
array = np.array(value, copy=True, order="C")
array.setflags(write=False)
owned[name] = array
object.__setattr__(self, "features", MappingProxyType(owned))
src/lerobot/inference/policy_runner.py:195 PolicyRunner._batch
def _batch(self, observation: ObservationSnapshot) -> dict[str, Any]:
if set(observation.features) != {feature.name for feature in self.capabilities.features}:
raise ValueError("Observation feature names differ from the serving contract.")
if len(observation.task) > self.max_text_input:
raise ValueError("Instruction exceeds the configured text-input limit.")
batch: dict[str, Any] = {}
for feature in self.capabilities.features:
array = observation.features[feature.name]
if array.shape != feature.shape or array.dtype != np.dtype(feature.dtype):
raise ValueError(
f"Observation shape/dtype differs from the serving contract: {feature.name}."
)
if array.dtype.kind == "f" and not np.isfinite(array).all():
raise ValueError(f"Observation contains non-finite values: {feature.name}.")
tensor = torch.from_numpy(array.copy())
if feature.kind == "rgb":
tensor = tensor.permute(2, 0, 1).contiguous().to(torch.float32).div_(255)
batch[feature.name] = tensor.unsqueeze(0)
batch["task"] = [observation.task]
batch["robot_type"] = self.robot_type
return batch
src/lerobot/inference/contracts.py:34 FeatureSpec
class FeatureSpec:
"""Named canonical values, ordered components, and semantic conventions."""
name: str
shape: tuple[int, ...]
dtype: str
kind: str = "tensor"
names: tuple[str, ...] = ()
semantics: str = ""
def __post_init__(self) -> None:
"""Reject unsupported modalities and ambiguous feature metadata."""
object.__setattr__(self, "shape", tuple(self.shape))
object.__setattr__(self, "names", tuple(self.names))
if not self.name or not self.semantics.strip():
raise ValueError("Feature names and explicit semantic conventions are required.")
if self.kind not in {"tensor", "rgb"}:
raise ValueError(f"Unsupported feature modality: {self.kind!r}")
if len(self.shape) > 4 or any(type(dim) is not int or dim <= 0 for dim in self.shape):
raise ValueError(f"Invalid feature shape: {self.shape!r}")
if self.dtype not in {"bool", "uint8", "int32", "int64", "float32", "float64"}:
raise ValueError(f"Unsupported feature dtype: {self.dtype!r}")
if self.kind == "rgb" and (len(self.shape) != 3 or self.shape[-1] != 3 or self.dtype != "uint8"):
raise ValueError("RGB features require HWC uint8 with three channels.")
if self.names and (len(self.shape) != 1 or len(self.names) != self.shape[0]):
raise ValueError("Ordered component names must match a one-dimensional feature.")
if len(set(self.names)) != len(self.names):
raise ValueError("Feature component names must be unique.")

## Slide 5
1 · MAP THE SYSTEM
Different identifiers prevent different mistakes
A sequence number does not replace session identity or freshness.
instance + session
Which server process and exclusive client owner?
generation + task_version
Is this motion epoch and instruction still current?
request_id + sequence
Which operation, and has it already been consumed?
observation_id + cursor
Which captured state and committed action position?
Client monotonic time answers “how old?”; the action cursor answers “how much was committed?”
05
Notes: The server instance changes on restart. A session identifies exclusive ownership. Generation fences reset/invalidation boundaries; task_version distinguishes retargets, including A → B → A; setting the already-current text is a no-op. Request IDs correlate replies, while a monotonic data sequence prevents re-execution after bounded request-ID history is evicted.
The observation action_cursor is local scheduling metadata. It is separate from the wire request sequence. It counts policy endpoints already handed to interpolation, not encoder measurements or server time.
Client capture times are carried through the response as opaque provenance on the server. The client evaluates age with its own monotonic clock; the server reports local durations. Synchronized wall clocks are not required.
Review question: Can identical task text make an old in-flight answer current again?
Answer: No. Version/generation/query intent checks still distinguish it from the new request.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/remote_inference/protocol.py:88 — Envelope
src/lerobot/inference/contracts.py:152 — ActionProvenance
tests/remote_inference/test_session.py:139 — test_evicted_request_identity_cannot_be_replayed
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/remote_inference/protocol.py:88 Envelope
class Envelope:
"""Every data message has a correlation identity; negotiation permits empty instance/session IDs."""
message_type: MessageType | str
instance_id: str = ""
session_id: str = ""
generation: int = 0
request_id: str = ""
body: dict[str, Any] = field(default_factory=dict)
version: int = PROTOCOL_VERSION
def __post_init__(self) -> None:
"""Validate correlation fields before decoding potentially large bodies."""
if type(self.version) is not int or self.version != PROTOCOL_VERSION:
raise ProtocolError(ErrorCode.PROTOCOL, f"Unsupported protocol version: {self.version!r}")
try:
object.__setattr__(self, "message_type", MessageType(self.message_type))
except (ValueError, TypeError) as exc:
raise ProtocolError(ErrorCode.MALFORMED, "Unknown message type") from exc
if type(self.generation) is not int or not 0 <= self.generation < 2**63:
raise ProtocolError(ErrorCode.MALFORMED, "Invalid execution generation")
for label in ("instance_id", "session_id", "request_id"):
value = getattr(self, label)
if not isinstance(value, str) or len(value) > _MAX_IDENTIFIER:
raise ProtocolError(ErrorCode.MALFORMED, f"Invalid {label}")
if value:
validate_segment(value, label)
if not isinstance(self.body, dict) or any(not isinstance(key, str) for key in self.body):
raise ProtocolError(ErrorCode.MALFORMED, "Message body must be a string-keyed map")
if self.message_type in {
MessageType.OBSERVATION,
MessageType.ACTION,
[Excerpt continues in the source file.]
src/lerobot/inference/contracts.py:152 ActionProvenance
class ActionProvenance:
"""Source identity carried by every queued action, including across merges."""
capture_time: float
task: str
task_version: int = 0
observation_id: str = ""
request_id: str = ""
generation: int = 0
session_id: str = ""
server_instance_id: str = ""
artifact_identity: str = ""
# The primary IDs identify the incoming prediction. capture_time is the
# conservative age bound; this summary retains the oldest original source.
oldest_contributor: ActionSource | None = None
contributor_count: int = 1
contributor_digest: str = ""
tests/remote_inference/test_session.py:139 test_evicted_request_identity_cannot_be_replayed
def test_evicted_request_identity_cannot_be_replayed(worker):
session = admit(worker)
first = action_request(worker, session)
assert worker.submit(first).result(2).message_type is MessageType.ACTION
for _ in range(128):
assert worker.submit(action_request(worker, session)).result(2).message_type is MessageType.ACTION
assert first.request_id not in worker._seen
assert_error(worker.submit(first).result(2), ErrorCode.STALE)

## Slide 6
2 · TRACE ONE REQUEST
Admission establishes a complete contract
Description, negotiation and readiness all happen before action requests.
Describe
protocol + build
capabilities + schema
→
Validate
rate + semantics
mode + merge
settings
→
Open
reserve owner
reset through worker
→
Ready
bind session channels
confirm subscribers
Version logs help diagnosis. Protocol and capability checks determine compatibility.
06
Notes: RemoteClient.connect obtains a descriptor. admit compares features, action representation, interval and semantics. For alignment/blending it sends required capabilities and exact chunk settings; plain append uses compatible defaults. Alignment and blending require explicit support, even though the protocol major remains 1.
SessionWorker validates the open request and reserves one session. The worker performs reset before acknowledging admission. The client verifies the acknowledgment and establishes session-scoped channels and presence. Data publication waits for subscriber readiness.
Two peers need not have identical Git hashes or package versions. They must satisfy the actual protocol and requested feature contract. The loaded-build log helps reveal an outdated running server; it is not a substitute for negotiation.
Review question: What happens if an older server does not advertise alignment?
Answer: A client requiring alignment fails admission rather than silently falling back to append.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/remote_inference/client.py:186 — RemoteClient.admit
src/lerobot/remote_inference/server.py:338 — SessionWorker._validate_open
tests/remote_inference/test_session.py:104 — test_unknown_required_capability_rejects_before_session_admission
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/remote_inference/client.py:186 RemoteClient.admit
def admit(
self,
*,
features: tuple[FeatureSpec, ...],
action_feature: FeatureSpec,
semantics: str,
action_interval: float,
mode: str,
) -> None:
"""Validate the robot contract and acquire one exclusive session."""
caps = self.capabilities
if (
features != caps.features
or action_feature != caps.action_feature
or semantics != self.descriptor["semantics"]
or not math.isclose(action_interval, caps.action_interval, rel_tol=1e-6)
or ExecutionMode(mode) not in caps.modes
):
raise ProtocolError(ErrorCode.INCOMPATIBLE, "Robot features, conventions, cadence or mode differ")
required = required_chunk_capabilities(self.chunk_settings)
if required:
if mode != ExecutionMode.CHUNK:
raise ProtocolError(ErrorCode.INCOMPATIBLE, "Aligned merge requires chunk execution")
advertised = self.descriptor.get("execution_contracts", [])
if not isinstance(advertised, list) or any(name not in advertised for name in required):
raise ProtocolError(
ErrorCode.UNSUPPORTED,
"Server does not support the requested chunk alignment/blending contract; update the server",
)
try:
self.blend_indices = validate_chunk_contract(
self.chunk_settings, caps, self.descriptor.get("blendable_components", [])
[Excerpt continues in the source file.]
src/lerobot/remote_inference/server.py:338 SessionWorker._validate_open
def _validate_open(self, body: dict[str, Any]) -> None:
caps = self.runner.capabilities
required = body.get("required_capabilities", [])
if not isinstance(required, list) or any(
not isinstance(name, str) or name not in self.execution_contracts for name in required
):
raise ProtocolError(ErrorCode.UNSUPPORTED, "Unknown required protocol capabilities")
settings = body.get("chunk_settings", chunk_settings("append", 0, 0.5, []))
try:
validate_chunk_contract(settings, caps, self.blendable_components)
except ValueError as exc:
raise ProtocolError(ErrorCode.INCOMPATIBLE, str(exc)) from exc
if required != required_chunk_capabilities(settings):
raise ProtocolError(ErrorCode.INCOMPATIBLE, "Required capabilities differ from chunk_settings")
if settings["chunk_merge"] == "aligned" and body.get("mode") != ExecutionMode.CHUNK:
raise ProtocolError(ErrorCode.INCOMPATIBLE, "Aligned merge requires chunk execution")
if body.get("expected_artifact") not in (None, self.artifact_identity):
raise ProtocolError(ErrorCode.INCOMPATIBLE, "Deployed artifact identity differs")
if body.get("semantics") != self.semantics:
raise ProtocolError(ErrorCode.INCOMPATIBLE, "Robot/action semantic profile differs")
if ExecutionMode(body["mode"]) not in caps.modes:
raise ProtocolError(ErrorCode.UNSUPPORTED, "Requested execution mode is unavailable")
if not math.isclose(float(body["action_interval"]), caps.action_interval, rel_tol=1e-6):
raise ProtocolError(ErrorCode.INCOMPATIBLE, "Policy action interval differs")
features = tuple(FeatureSpec(**value) for value in body["features"])
action = FeatureSpec(**body["action_feature"])
if features != caps.features or action != caps.action_feature:
raise ProtocolError(ErrorCode.INCOMPATIBLE, "Ordered feature schema or semantics differ")
if body.get("encoding") not in {"raw", "jpeg"}:
raise ProtocolError(ErrorCode.UNSUPPORTED, "Unsupported image encoding")
tests/remote_inference/test_session.py:104 test_unknown_required_capability_rejects_before_session_admission
def test_unknown_required_capability_rejects_before_session_admission(worker):
request = open_request(worker)
request.body["required_capabilities"] = ["future-observation-history"]
assert_error(worker.submit(request).result(2), ErrorCode.UNSUPPORTED)
assert worker.session_id is None

## Slide 7
2 · TRACE ONE REQUEST
A control tick never waits for inference
The strategy offers an observation, then dispatches only permitted local motion.
Observe
hardware sample
robot processing
→
Anchor
notify_observation
latest snapshot
→
Commit
get_action / pop
only if needed
→
Dispatch
interpolate + recheck
robot processor +
send
Observation anchoring precedes the next policy-endpoint commitment on the same thread.
07
Notes: The base strategy reads raw hardware on every motor tick; processing and notification are gated to policy-endpoint boundaries. With interpolation enabled, intermediate motor ticks reuse processed observations; they do not manufacture new policy snapshots.
notify_observation constructs an owned ObservationSnapshot and anchors it to the runtime cursor. send_next_action handles the interpolator. It asks for a new canonical endpoint only when needed, checks permission again around dispatch, then processes and sends the local command.
A control tick can continue while RemoteClient.infer waits elsewhere. This is not a hard-real-time guarantee: synchronous hardware reads, camera waits and local processing can still delay a tick. Revoking dispatch also clears the interpolator, so an already cached intermediate command cannot keep moving after a hold or fault.
Review question: Is checking permission only when popping a chunk sufficient?
Answer: No. Interpolation can emit more motor commands without another pop, so permission must be checked on every dispatch tick.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/rollout/strategies/core.py:171 — RolloutStrategy._process_observation_and_notify
src/lerobot/rollout/strategies/core.py:443 — send_next_action
src/lerobot/rollout/inference/remote.py:245 — RemoteInferenceEngine.notify_observation
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/rollout/strategies/core.py:171 RolloutStrategy._process_observation_and_notify
def _process_observation_and_notify(
self, processors: ProcessorContext, obs_raw: RobotObservation
) -> RobotObservation:
"""Run the observation processor and notify the engine — throttled to policy ticks.
Callers are responsible for calling ``robot.get_observation()`` every loop
iteration so ``obs_raw`` stays fresh for the action post-processor. This
helper gates only the comparatively expensive bits — the processor pipeline
and ``engine.notify_observation`` — to fire when the interpolator signals
it needs a new action (once per ``interpolation_multiplier`` ticks). On
interpolated ticks the cached ``obs_processed`` is reused.
With ``interpolation_multiplier == 1`` this is equivalent to the unthrottled
path: ``needs_new_action()`` is True every tick.
The cache is implicitly invalidated whenever ``interpolator.reset()`` is
called (warmup completion, DAgger phase transitions back to AUTONOMOUS),
because reset makes ``needs_new_action()`` return True on the next call.
"""
if self._cached_obs_processed is None or self._require_interpolator().needs_new_action():
obs_processed = processors.robot_observation_processor(obs_raw)
self._require_engine().notify_observation(obs_processed)
self._cached_obs_processed = obs_processed
return self._cached_obs_processed
src/lerobot/rollout/strategies/core.py:443 send_next_action
def send_next_action(
obs_processed: dict,
obs_raw: dict,
ctx: RolloutContext,
interpolator: ActionInterpolator,
timer: CycleTimer | None = None,
) -> dict | None:
"""Dispatch the next action to the robot.
Pulls the next action tensor from the inference engine, feeds the
interpolator, and sends the interpolated action through the
``robot_action_processor`` to the robot. Works identically for
sync and async backends — the rollout strategy never needs to branch.
When *timer* is given, the engine pull and the robot send are timed as the
``infer`` and ``send`` steps of its cadence summary, and a tick with no action
to send is counted there. Note that on async backends ``infer`` is only a
queue pull — inference runs off-thread, so its latency surfaces as starved
ticks rather than as loop-body time.
Returns the action dict that was sent, or ``None`` if no action was
ready (e.g. empty async queue, interpolator not yet primed).
"""
engine = ctx.policy.inference
engine.begin_control_tick()
features = ctx.data.dataset_features
ordered_keys = ctx.data.ordered_action_keys
# ``nullcontext`` accepts (and ignores) the section name, so it stands in for
# ``timer.section`` verbatim when no timer was passed.
section = timer.section if timer is not None else contextlib.nullcontext
def dispatch_permitted() -> bool:
[Excerpt continues in the source file.]
src/lerobot/rollout/inference/remote.py:245 RemoteInferenceEngine.notify_observation
def notify_observation(self, obs: dict) -> None:
sampled = self._robot.observation_time
if sampled is None:
sampled = time.monotonic()
frame = build_dataset_frame(self._features, obs, prefix="observation")
mapped = {self._rename_map.get(key, key): value for key, value in frame.items()}
if len(mapped) != len(frame):
self._fault("Feature mapping contains a collision")
return
# Mapping is applied once here; server processors require an empty rename map.
with self._task_lock:
task, version = self._task, self._task_version
snapshot = ObservationSnapshot(mapped, sampled, task, version, uuid4().hex)
with self._lock:
# Sampling and endpoint commits both belong to this control thread;
# no pop occurs between the hardware read and this anchor. Workers
# may replace the future, but never advance the commitment cursor.
if self.config.chunk_merge == "aligned":
snapshot = self.runtime.anchor_observation(snapshot)
self._observation = snapshot

## Slide 8
2 · TRACE ONE REQUEST
Concurrency is deliberately bounded
New observations replace the waiting snapshot; they do not form a backlog.
Control thread
latest observation slot → ChunkRuntime / ActionQueue
Short shared-state operations; local permission checked each motor tick.
Client worker
ordered control → eligible latest snapshot → infer → accept
One inference in flight. Network waits happen here.
Server worker
bounded command handoff → one policy / processor operation
Open, reset, action, language and close share serialized ownership.
Bounded queues prevent hidden work accumulation; freshness checks still decide usability.
08
Notes: The engine lock protects observation/control/hold coordination, the task lock orders retargets with acceptance, and the runtime lock protects generation, requests and the queue interaction. ActionQueue has its own atomic snapshot/replace operations.
The server has bounded callback handoffs and one outstanding inference admission. Control operations can be queued behind a current model call; they do not reset mutable state concurrently with it.
When reading a method, identify its calling thread and the lock held before interpreting its assignments. A thread-safe container alone does not establish the ordering between observation capture, commitment and result acceptance.
Review question: If inference is slow, should the client save every camera frame for later?
Answer: No. This current-observation runner keeps the latest waiting snapshot and only one in-flight request. A frame backlog would increase source age.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/rollout/inference/remote.py:374 — RemoteInferenceEngine._loop
src/lerobot/remote_inference/server.py:208 — SessionWorker.submit
src/lerobot/policies/rtc/action_queue.py:127 — ActionQueue.snapshot
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/rollout/inference/remote.py:374 RemoteInferenceEngine._loop
def _loop(self) -> None:
try:
while not self._stop_event.is_set() and not self.failed:
# Control-thread dispatch only queues bounded diagnostics. Log
# from this worker so first-dispatch reporting adds no motor I/O.
with self.runtime.lock:
dispatch_events = list(self.runtime.dispatch_events)
self.runtime.dispatch_events.clear()
for event in dispatch_events:
self._event("first_dispatch", **event)
with self._lock:
control = self._control
observation = self._observation
hold_ready = self._hold_requested and self._hold_acknowledged
if control is not None:
# Language invalidation must be acknowledged by the motor thread
# before submitting any server-side generation operation.
if self._hold_requested and not hold_ready:
self._stop_event.wait(0.002)
continue
operation, generation = control
self.client.control(operation, generation)
with self._lock:
if self._control == control:
self._control = None
continue
if not self.runtime.active or observation is None:
self.runtime.check_deadlines()
self._stop_event.wait(0.002)
continue
if hold_ready:
with self._lock:
[Excerpt continues in the source file.]
src/lerobot/remote_inference/server.py:208 SessionWorker.submit
def submit(self, message: Envelope) -> Future[Envelope]:
"""Validate and enqueue work without running policy code on the caller's thread."""
future: Future[Envelope] = Future()
with self._lock:
try:
if message.message_type is MessageType.DESCRIBE:
future.set_result(
Envelope(
MessageType.DESCRIPTOR,
self.instance_id,
request_id=message.request_id,
body=self._descriptor_locked(),
)
)
return future
if message.instance_id != self.instance_id:
raise ProtocolError(ErrorCode.STALE, "Server instance does not match")
if message.message_type is MessageType.OPEN:
if not message.request_id:
raise ProtocolError(ErrorCode.MALFORMED, "Open operation ID is required")
if message.request_id in self._opens:
return self._opens[message.request_id]
if self._session is not None:
state = self._session_diagnostics_locked()
detail = (
f"Deployment owned by session={state['owner']}; "
f"admission_blocker={state['admission_blocker']} "
f"client_present={state['client_present']} "
f"absence_grace_remaining_s={state['absence_grace_remaining_s']} "
f"cleanup_pending={state['cleanup_pending']} "
f"inference_pending={state['inference_pending']}. "
"A new session requires the previous owner's close/reset to finish; "
[Excerpt continues in the source file.]
src/lerobot/policies/rtc/action_queue.py:127 ActionQueue.snapshot
def snapshot(self) -> QueueSnapshot:
"""Copy cursor, both continuations and their provenance under one lock."""
with self.lock:
return QueueSnapshot(
generation=self._generation,
cursor=self._cursor,
index=self.last_index,
model_actions=None
if self.original_queue is None
else self.original_queue[self.last_index :].clone(),
canonical_actions=None if self.queue is None else self.queue[self.last_index :].clone(),
provenance=tuple(self._provenance_queue[self.last_index :]),
)

## Slide 9
2 · TRACE ONE REQUEST
The request crosses a bounded transport
Control uses query/reply; observations and results use session channels.
ChunkRequest
capture + continuation
generation + local
timing
→
RemoteClient
Envelope + sequence
encode observation
→
Zenoh / server
bounded handoff
validate and enqueue
→
Action reply
decode + correlate
canonical chunk
No unbounded replay queue and no policy work inside transport callbacks.
09
Notes: RemoteClient.infer constructs an observation request, including the RTC continuation when required. The MessagePack codec preserves tensor metadata, enforces configured bounds and uses raw RGB or explicitly selected JPEG encoding. JPEG is lossy; it is a deployment tradeoff, not an exact-byte transport.
The server validates instance/session/generation and data shape, rejects duplicate or non-increasing data requests, and hands accepted work to SessionWorker. The envelope header is correlated before the tensor body is decoded; the validated reply becomes an ActionChunk.
The transport is not an automatic action retry/replay mechanism. Readiness, bounded waiting and terminal errors are explicit. A client may continue locally buffered valid motion during a transient absence, but a terminal fault cannot be undone by a later packet.
Review question: Why does the server track a monotonic sequence as well as recent request IDs?
Answer: Its request-ID cache is bounded. The sequence rejects a replay even after that ID has aged out of the cache.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/remote_inference/client.py:382 — RemoteClient.infer
src/lerobot/remote_inference/server.py:208 — SessionWorker.submit
src/lerobot/remote_inference/codec.py:279 — encode_message
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/remote_inference/client.py:382 RemoteClient.infer
def infer(self, request: ChunkRequest, *, cancelled: Callable[[], bool] = lambda: False) -> ActionChunk:
"""Exchange one action request and validate its identity, execution context and values."""
body = self._observation_body(request.observation)
model_continuation = request.continuation.model_actions
canonical_continuation = request.continuation.canonical_actions
body.update(
{
"delay": request.delay,
"model_continuation": model_continuation
if model_continuation is not None and len(model_continuation)
else None,
"canonical_continuation": canonical_continuation
if canonical_continuation is not None and len(canonical_continuation)
else None,
"cursor": request.continuation.cursor,
}
)
if self.chunk_settings["chunk_merge"] == "aligned":
body["observation_cursor"] = request.observation.action_cursor
envelope = Envelope(
MessageType.OBSERVATION,
self.instance_id,
self.session_id,
request.generation,
request.request_id,
body,
)
response = self._exchange(envelope, "/obs", self._actions, self.config.action_timeout_s, cancelled)
self._validate_context(response, body, MessageType.ACTION)
actions = response.body.get("canonical_actions")
model = response.body.get("model_actions")
caps = self.capabilities
[Excerpt continues in the source file.]
src/lerobot/remote_inference/server.py:208 SessionWorker.submit
_remember(self._controls, message.request_id, future, 32)
elif message.message_type in {MessageType.OBSERVATION, MessageType.LANGUAGE_REQUEST}:
if not session.ready or session.closing or session.faulted:
raise ProtocolError(ErrorCode.STALE, "Session is not accepting inference")
if message.generation != session.generation:
raise ProtocolError(ErrorCode.STALE, "Generation has not been acknowledged")
if message.request_id in self._seen:
raise ProtocolError(ErrorCode.STALE, "Duplicate or completed request")
if session.busy:
raise ProtocolError(
ErrorCode.BUSY, "One inference operation is already outstanding"
)
self._validate_data(message)
if message.body["sequence"] <= session.last_sequence:
raise ProtocolError(ErrorCode.STALE, "Request sequence was already consumed")
if self._commands.full():
raise ProtocolError(ErrorCode.BUSY, "Policy command queue is full")
session.busy = True
session.last_sequence = message.body["sequence"]
_remember(self._seen, message.request_id, None)
else:
raise ProtocolError(ErrorCode.MALFORMED, "Unexpected request message type")
self._commands.put_nowait((message, future, time.monotonic()))
except (ProtocolError, ValueError, KeyError, TypeError, Full) as exc:
code = (
exc.code
if isinstance(exc, ProtocolError)
else ErrorCode.BUSY
if isinstance(exc, Full)
else ErrorCode.MALFORMED
)
details = exc.details if isinstance(exc, ProtocolError) else None
[Excerpt continues in the source file.]
src/lerobot/remote_inference/codec.py:279 encode_message
def encode_message(envelope: Envelope, limits: CodecLimits = CodecLimits()) -> bytes:
"""Encode only supported, finite values into an explicitly typed envelope."""
require_package("msgpack", "remote")
envelope.__post_init__()
record = {
"version": envelope.version,
"message_type": str(envelope.message_type),
"instance_id": envelope.instance_id,
"session_id": envelope.session_id,
"generation": envelope.generation,
"request_id": envelope.request_id,
"body": envelope.body,
}
encoded = msgpack.packb(_encode_value(record, _Budget(limits)), use_bin_type=True)
if len(encoded) > limits.max_payload_bytes:
raise _malformed("Encoded message exceeds byte limit")
return encoded

## Slide 10
2 · TRACE ONE REQUEST
PolicyRunner is the model boundary
The direct chunk call must reproduce the policy’s inference preparation.
_batch
validate wire values
create batched
tensors
→
preprocessor
saved normalization
resize / tokenize
→
predict_action_chunk
[1, prediction_steps,
A]
validate model output
→
postprocessor
canonical coordinates
validate then slice
Plain execution uses execution_steps. RTC keeps the declared prediction horizon.
10
Notes: The runner does not call select_action. The direct predict_action_chunk implementation must prepare everything it needs without depending on observation history or queues that only select_action populates.
It validates the full predicted tensor before postprocessing, saves a detached model-space copy, validates the canonical tensor and then applies the plain execution slice. The current default runner requires the same declared dimensions before and after postprocessing; a padded model width cannot be silently accepted just because a later processor crops it.
Guided RTC requires a local autograd correction. The outer call uses no_grad while disabling inference_mode for guided RTC, allowing the policy to enable gradients for that correction. This was one of the fixes retained from hardware testing.
Review question: Why does a working synchronous checkpoint not automatically prove remote compatibility?
Answer: select_action may collect history, crop a different horizon or perform preparation that direct chunk prediction does not. The remote contract has to describe the actual direct path.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/policy_runner.py:217 — PolicyRunner.predict
src/lerobot/inference/policy_runner.py:291 — PolicyRunner._validate_actions
src/lerobot/policies/pretrained.py:307 — PreTrainedPolicy.chunk_inference_spec
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/policy_runner.py:217 PolicyRunner.predict
# permits that override; inference_mode would suppress its gradient graph.
with torch.inference_mode(mode is not ExecutionMode.RTC_GUIDED), torch.no_grad():
prepared = self.preprocessor(self._batch(observation))
preprocessed_at = time.perf_counter()
kwargs: dict[str, Any] = {}
if mode != ExecutionMode.CHUNK:
prefix = self._prepare_continuation(model_continuation, canonical_continuation)
if inference_delay < 0:
raise ValueError("RTC delay must be nonnegative.")
if prefix is None and inference_delay:
raise ValueError("RTC delay requires a real continuation prefix.")
if mode == ExecutionMode.RTC_TRAINED:
available = 0 if model_continuation is None else len(model_continuation)
if inference_delay > min(
self.capabilities.training_max_delay, available, self.capabilities.rtc_horizon
):
raise ValueError(
"Trained RTC delay exceeds checkpoint or available continuation limits."
)
kwargs = {"inference_delay": inference_delay, "prev_chunk_left_over": prefix}
predicted = self.policy.predict_action_chunk(prepared, **kwargs)
predicted_at = time.perf_counter()
self._validate_actions(predicted)
# A postprocessor may modify its argument. Preserve model coordinates
# before invoking the paired canonical postprocessor.
original = predicted.detach().clone()
canonical = self.postprocessor(predicted)
self._validate_actions(canonical)
steps = (
self.capabilities.execution_steps
if mode == ExecutionMode.CHUNK
else self.capabilities.prediction_steps
)
canonical = canonical[0, :steps].detach().to(device="cpu", dtype=torch.float32).clone()
model = (
original[0, :steps].detach().to(device="cpu", dtype=torch.float32).clone()
if mode != ExecutionMode.CHUNK
else None
)
finished = time.perf_counter()
return ActionChunk(
model_actions=model,
[Excerpt continues in the source file.]
src/lerobot/inference/policy_runner.py:291 PolicyRunner._validate_actions
def _validate_actions(self, actions: torch.Tensor) -> None:
expected = (1, self.capabilities.prediction_steps, self.capabilities.action_feature.shape[0])
if not isinstance(actions, torch.Tensor) or tuple(actions.shape) != expected:
raise ValueError(f"Policy/processor must return action shape {expected}.")
if not actions.is_floating_point() or not torch.isfinite(actions).all():
raise ValueError("Policy/processor returned non-finite or non-floating actions.")
src/lerobot/policies/pretrained.py:307 PreTrainedPolicy.chunk_inference_spec
def chunk_inference_spec(self) -> ChunkPolicySpec:
"""Declare the default current-observation chunk-serving author contract.
Inheriting this implementation declares that ``predict_action_chunk`` does
every preparation needed by direct callers, accepts the complete current
observation, and returns ``[B, chunk_size, A]`` in model coordinates. Its
canonical processor pair must support whole chunks. ``n_action_steps`` is
the ordinary playback slice; RTC retains the full prediction horizon.
A policy requiring select_action-only preparation, other action layouts,
or temporal sampling must override this method and reject unsupported
configurations or provide a custom runner. Method presence or a successful
warmup is not evidence for this contract. Policy/processor state is allowed
only within an exclusive session and reset() must clear it for a new run.
"""
config = self.config
if config.n_obs_steps != 1:
raise ValueError("Chunk serving requires n_obs_steps=1; observation history is unsupported.")
for field_name in (
"observation_delta_indices",
"image_observation_delta_indices",
"state_observation_delta_indices",
):
indices = getattr(config, field_name, None)
if indices is not None and list(indices) != [0]:
raise ValueError(f"Chunk serving cannot sample temporal history ({field_name}).")
if getattr(config, "temporal_ensemble_coeff", None) is not None:
raise ValueError("Chunk serving does not support temporal ensembling.")
if getattr(config, "use_visual_memory", False) or getattr(config, "use_proprioceptive_memory", False):
raise ValueError(
"Chunk serving cannot sample observation memory at the required control cadence."
)
[Excerpt continues in the source file.]

## Slide 11
2 · TRACE ONE REQUEST
Receiving a result does not authorize motion
Correlation, runtime acceptance and dispatch permission are separate gates.
Client checks
reply type / identity
context + tensor
shape
→
Runtime checks
pending request +
epoch
task + age + deadline
→
Merge checks
usable future suffix
mode-specific
constraints
→
Dispatch checks
active + unheld
source still fresh
A valid result can still become unusable before its first motor command.
11
Notes: RemoteClient checks that the reply belongs to the negotiated context and its request. ChunkRuntime.accept then checks the currently pending request and execution generation, current task version, elapsed deadlines, source age and chunk structure.
An aligned result with no usable suffix is rejected without destroying an otherwise eligible old future. If no subsequent usable result arrives, the existing age/deadline/exhaustion rules still apply. A stale source-age violation is a terminal fault, which is different from simply rejecting an obsolete result.
At pop and on interpolated ticks, dispatch_allowed checks again. Old buffered actions do not acquire the timestamp of the newest result. Provenance remains attached to the values it actually describes.
Review question: If reset occurs while the network worker is waiting, can that reply refill the new run?
Answer: No. Invalidation changes generation and clears the pending request locally. Acceptance cannot restore the revoked epoch.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/remote_inference/client.py:449 — RemoteClient._validate_context
src/lerobot/inference/execution.py:263 — ChunkRuntime.accept
src/lerobot/inference/execution.py:434 — ChunkRuntime.dispatch_allowed
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/remote_inference/client.py:449 RemoteClient._validate_context
def _validate_context(self, response: Envelope, body: dict, expected: MessageType) -> None:
context_keys = ["artifact_identity", "observation_id", "capture_time", "task", "task_version"]
if expected is MessageType.ACTION and self.chunk_settings["chunk_merge"] == "aligned":
context_keys.extend(["observation_cursor", "cursor"])
if any(type(response.body.get(key)) is not int for key in ("observation_cursor", "cursor")):
raise ProtocolError(
ErrorCode.MALFORMED, "Result action cursor context differs from its request"
)
if response.message_type is not expected or any(
response.body.get(key) != body[key] for key in context_keys
):
raise ProtocolError(ErrorCode.MALFORMED, "Result execution context differs from its request")
src/lerobot/inference/execution.py:263 ChunkRuntime.accept
def accept(self, request: ChunkRequest, chunk: ActionChunk, *, task_version: int) -> bool:
"""Validate context and timing, then atomically merge with original provenance."""
with self.lock:
self.last_accept = {"accepted": False}
self.check_deadlines()
if self.failure or self.pending is not request or request.generation != self.generation:
return False
self.pending = None
if request.observation.task_version != task_version:
return False
now = self.clock()
elapsed = now - request.submitted_at
self._completed += 1
if self._completed > 1: # cold start is not a steady-state action latency
self.turnarounds.append(elapsed)
if now - request.observation.capture_time > self.max_age:
self.fault("Action result source observation is too old")
return False
actions = chunk.canonical_actions
model = chunk.model_actions if chunk.model_actions is not None else actions
if (
actions.ndim != 2
or model.ndim != 2
or len(actions) != len(model)
or not len(actions)
or type(chunk.execution_steps) is not int
or not 0 < chunk.execution_steps <= len(actions)
or not torch.isfinite(actions).all()
or not torch.isfinite(model).all()
):
self.fault("Invalid action chunk")
return False
[Excerpt continues in the source file.]
src/lerobot/inference/execution.py:434 ChunkRuntime.dispatch_allowed
def dispatch_allowed(self) -> bool:
"""Check permission and the committed endpoint's age on every motor tick."""
with self.lock:
self.check_deadlines()
if self.failure or not self.active or self.held:
return False
if self.current is not None and self.clock() - self.current.capture_time > self.max_age:
self.fault("Dispatched action source observation is too old")
return False
return self.current is not None or not self.queue.empty()

## Slide 12
3 · READ EXECUTION
The cursor counts committed endpoints
Commitment happens when pop hands a target to interpolation.
Measured position
Where sensors report the robot is now.
Committed endpoint
A target handed to interpolation; chunk merging cannot replace it.
Queued future
Targets still owned by ActionQueue; eligible for replacement.
Atomic snapshot
Cursor + generation + both action spaces + provenance together.
With interpolation ×2, two motor ticks still consume only one policy endpoint.
12
Notes: ActionQueue.get_with_provenance advances the commitment cursor. An endpoint is already committed even if the robot is still moving toward it through interpolation. Alignment must not reinterpret that endpoint as replaceable future. A hold, reset or fault can still revoke interpolation and dispatch permission.
The observation is anchored before the next endpoint is popped. A later request also captures an atomic continuation snapshot. These are different moments: aligned trimming uses the observation anchor, including progress that happened before request submission.
Do not use qsize as a proxy for cursor advance: replacement changes queue length. Snapshot consistency also matters for RTC, which needs paired canonical/model continuation and provenance from the same moment.
Review question: Does cursor 103 mean the robot physically reached endpoint 102?
Answer: No. It means 103 endpoints have been committed in that queue epoch. The latest may still be interpolating.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/policies/rtc/action_queue.py:107 — ActionQueue.get_with_provenance
src/lerobot/policies/rtc/action_queue.py:127 — ActionQueue.snapshot
src/lerobot/inference/execution.py:143 — ChunkRuntime.anchor_observation
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/policies/rtc/action_queue.py:107 ActionQueue.get_with_provenance
def get_with_provenance(self) -> tuple[Tensor, str | None, Any] | None:
"""Commit one action, returning its original request provenance atomically."""
with self.lock:
if self.queue is None or self.last_index >= len(self.queue):
return None
if self._task_queue is not None and len(self._task_queue) != len(self.queue):
# A mismatch means some mutation broke the action/task lockstep.
raise RuntimeError(
f"ActionQueue task labels out of sync with actions "
f"({len(self._task_queue)} labels for {len(self.queue)} actions) — "
"a queue mutation broke the action/task lockstep invariant"
)
action = self.queue[self.last_index]
task = None if self._task_queue is None else self._task_queue[self.last_index]
provenance = self._provenance_queue[self.last_index] if self._provenance_queue else None
self.last_index += 1
self._cursor += 1
return action.clone(), task, provenance
src/lerobot/policies/rtc/action_queue.py:127 ActionQueue.snapshot
def snapshot(self) -> QueueSnapshot:
"""Copy cursor, both continuations and their provenance under one lock."""
with self.lock:
return QueueSnapshot(
generation=self._generation,
cursor=self._cursor,
index=self.last_index,
model_actions=None
if self.original_queue is None
else self.original_queue[self.last_index :].clone(),
canonical_actions=None if self.queue is None else self.queue[self.last_index :].clone(),
provenance=tuple(self._provenance_queue[self.last_index :]),
)
src/lerobot/inference/execution.py:143 ChunkRuntime.anchor_observation
def anchor_observation(self, observation: ObservationSnapshot) -> ObservationSnapshot:
"""Bind a control-thread sample before committing the next endpoint.
The sampling caller must not pop actions between capture and this call.
The rollout control thread owns both operations; a worker may replace
the future concurrently but cannot advance this commitment cursor.
"""
with self.lock:
return replace(
observation,
action_cursor=self.queue.snapshot().cursor,
execution_generation=self.generation,
)

## Slide 13
3 · READ EXECUTION
Append and alignment place a chunk differently
Illustrative example: capture at cursor 100; accept at cursor 103.
Incoming
A0
A1
A2
A3
A4
A5
A6
A7
Capture anchor = 100
Past slots
A0
A1
A2
3 slots passed before acceptance; cursor = 103
Aligned future
A3
A4
A5
A6
A7
Append instead keeps old future, then queues A0…A7.
Alignment removes 3 committed slots and replaces only the future: incoming A3…A7.
13
Notes: Assume an eight-action execution slice A0 through A7 and a capture anchor of 100. One endpoint commits before submission, and two more commit while inference runs. The current cursor is 103, so aligned trim is 103 − 100 = 3. It is not merely the two endpoints consumed after submission.
Append preserves the remaining old trajectory and places all eight new actions after it. This is bounded to one accepted successor, but the prediction waits and ages. Alignment replaces the uncommitted old future with A3 through A7.
At startup no endpoint has committed, so a slow first inference does not justify skipping the first actions. If trim consumes the entire execution slice, the aligned result is rejected; it never extends to unused prediction steps. The diagram is conceptual, not a measured robot trace.
Review question: If 500 ms pass but the cursor has not advanced, how many steps does plain alignment trim?
Answer: Zero. Plain alignment uses committed progress, not elapsed wall time. Freshness and deadlines are still checked separately.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/execution.py:386 — ChunkRuntime._accept_aligned
tests/inference/test_aligned_execution.py:59 — test_observation_anchor_accounts_for_progress_before_and_during_request
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/execution.py:386 ChunkRuntime._accept_aligned
def _accept_aligned(
self, request: ChunkRequest, actions: torch.Tensor, provenance: ActionProvenance, now: float
) -> bool:
snapshot = self.queue.snapshot()
anchor = request.observation.action_cursor
if anchor is None or request.observation.execution_generation != self.generation:
self.fault("Aligned result lacks its observation commitment anchor")
return False
trim = snapshot.cursor - anchor
self.last_accept["trimmed_actions"] = trim
if trim < 0 or trim >= len(actions):
self.last_accept["rejection"] = "no usable aligned suffix"
return False
future = actions[trim:].clone()
sources = [provenance] * len(future)
previous = snapshot.canonical_actions
overlap = min(len(previous), len(future)) if previous is not None else 0
self.last_accept["overlap_steps"] = overlap
if self.blend_indices and max(self.blend_indices) >= future.shape[1]:
self.fault("Blend component index exceeds canonical action dimensions")
return False
if previous is not None and self.blend_weight < 1:
for index in range(min(overlap, self.blend_steps)):
old = snapshot.provenance[index]
if (
old is None
or not self._same_context(old, provenance)
or not 0 <= now - old.capture_time <= self.max_age
):
continue
coordinates = list(self.blend_indices)
future[index, coordinates] = (1 - self.blend_weight) * previous[
[Excerpt continues in the source file.]
tests/inference/test_aligned_execution.py:59 test_observation_anchor_accounts_for_progress_before_and_during_request
def test_observation_anchor_accounts_for_progress_before_and_during_request():
rt, clock = runtime()
initial(rt, clock)
rt.pop() # committed endpoint 0, still potentially interpolating toward it
clock.now += 0.1
source = sample(rt, clock) # action zero assigned to endpoint 1
rt.pop() # endpoint 1 committed before request submission
request = rt.begin(source)
assert request.continuation.cursor == 2
rt.pop() # endpoint 2 committed during inference
clock.now += 0.001 # wall-time estimate is irrelevant to aligned trimming
assert rt.accept(request, result(request, 10), task_version=0)
assert rt.last_accept["trimmed_actions"] == 2
assert rt.queue.qsize() == 4
assert rt.pop()[0].tolist() == [12, 112]

## Slide 14
3 · READ EXECUTION
Blending operates on matching future slots
First align the trajectories. Then average eligible canonical coordinates.
Old future
slot k: joint = 10
gripper = 0
→
Incoming future
same slot k: joint = 18
gripper = 1
→
Blend: w = 0.5
joint = 0.5×10 +
0.5×18
= 14
→
Unselected axis
gripper = incoming 1
no implicit averaging
blend_weight is the incoming fraction; blend_steps limits eligible overlap.
14
Notes: The client explicitly selects blend_components from the deployment’s allowed continuous canonical coordinates. No gripper is automatically selected. The scalar numbers here are an illustrative arithmetic example, not a recommended joint command.
Only the first min(overlap, blend_steps) slots can blend, and only when context matches and the old source remains eligible. Non-selected coordinates remain the incoming values. There is no invented overlap at the end of a short old trajectory. Weight 1 is exact replacement.
Provenance keeps the oldest contributing capture time plus bounded contributor metadata. Repeated blending cannot disguise an old target as newly captured. This is a fixed weighted mixture, not an optimizer or a guarantee of task success. Relative model actions are postprocessed into canonical coordinates before plain blending.
Review question: Can a fresh incoming chunk make an old blended contribution fresh again?
Answer: No. The resulting action carries a conservative age based on the oldest contributing source.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/execution.py:386 — ChunkRuntime._accept_aligned
src/lerobot/inference/execution.py:367 — ChunkRuntime._blended_provenance
tests/inference/test_aligned_execution.py:283 — test_weighted_blend_matches_future_steps_and_keeps_gripper_incoming
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/execution.py:386 ChunkRuntime._accept_aligned
previous = snapshot.canonical_actions
overlap = min(len(previous), len(future)) if previous is not None else 0
self.last_accept["overlap_steps"] = overlap
if self.blend_indices and max(self.blend_indices) >= future.shape[1]:
self.fault("Blend component index exceeds canonical action dimensions")
return False
if previous is not None and self.blend_weight < 1:
for index in range(min(overlap, self.blend_steps)):
old = snapshot.provenance[index]
if (
old is None
or not self._same_context(old, provenance)
or not 0 <= now - old.capture_time <= self.max_age
):
continue
coordinates = list(self.blend_indices)
future[index, coordinates] = (1 - self.blend_weight) * previous[
index, coordinates
] + self.blend_weight * future[index, coordinates]
sources[index] = self._blended_provenance(old, provenance)
self.last_accept["blended_steps"] += 1
if self._last_action is not None:
self.last_accept["transition_delta"] = (future[0] - self._last_action).tolist()
if overlap and previous is not None:
self.last_accept["replacement_delta"] = (future[0] - previous[0]).tolist()
accepted = self.queue.replace_future(future, sources, snapshot=snapshot)
self.last_accept.update(
accepted=accepted,
usable_actions=len(future),
estimated_first_dispatch_source_age_s=now - sources[0].capture_time,
)
return accepted
src/lerobot/inference/execution.py:367 ChunkRuntime._blended_provenance
def _blended_provenance(old: ActionProvenance, new: ActionProvenance) -> ActionProvenance:
"""Summarize all contributing history in constant storage, without refreshing age."""
oldest = old.oldest_contributor or ActionSource(old.capture_time, old.observation_id, old.request_id)
if new.capture_time < oldest.capture_time:
oldest = ActionSource(new.capture_time, new.observation_id, new.request_id)
digest = hashlib.sha256(
json.dumps(
[old.contributor_digest, old.request_id, old.capture_time, new.request_id, new.capture_time],
separators=(",", ":"),
).encode()
).hexdigest()
return replace(
new,
capture_time=oldest.capture_time,
oldest_contributor=oldest,
contributor_count=min(old.contributor_count + 1, 2**63 - 1),
contributor_digest=digest,
)
tests/inference/test_aligned_execution.py:283 test_weighted_blend_matches_future_steps_and_keeps_gripper_incoming
def test_weighted_blend_matches_future_steps_and_keeps_gripper_incoming():
rt, clock = runtime(blend_steps=2, blend_weight=0.25, blend_indices=(0,))
initial(rt, clock)
committed = rt.pop()[0].clone()
clock.now += 0.1
request = rt.begin(sample(rt, clock))
assert rt.accept(request, result(request, 10), task_version=0)
assert committed.tolist() == [0, 100]
values = rt.queue.snapshot().canonical_actions
torch.testing.assert_close(values[:3], torch.tensor([[3.25, 110], [4.25, 111], [12, 112]]))
assert rt.last_accept["blended_steps"] == 2
assert rt.last_accept["overlap_steps"] == 5
assert rt.queue.qsize() == 6 # remaining old horizon does not accumulate
sources = rt.queue.snapshot().provenance
assert sources[0].capture_time == 10
assert sources[0].contributor_count == 2
assert sources[0].oldest_contributor.request_id
assert sources[2].capture_time == 10.1
assert sources[2].contributor_count == 1

## Slide 15
3 · READ EXECUTION
Refill is a playback threshold
The worker asks whether another prediction is needed, not whether a timer fired.
Δ = 1 / action_fps
Nominal seconds per policy endpoint
L = max recent steady turnaround
Up to 100 completed requests; first completion excluded
R_effective = max(refill_seconds, L + Δ)
Measured headroom can raise the configured threshold
request when queued_steps × Δ ≤ R_effective
Still requires permission, a fresh capture and no in-flight request
Larger refill usually requests earlier. Smaller refill lets more of the trajectory execute.
15
Notes: should_request gates both append and aligned chunk mode using remaining queued playback. Append also limits accepted successor storage. Aligned mode does not inherit that successor restriction because it replaces future targets.
The corrected aligned implementation waits for the playback threshold before begin reserves an observation. While it waits, the latest-snapshot slot keeps updating. At request time it can choose a recent capture rather than an observation saved when the worker first became free.
An aligned task change may bypass the playback threshold, but it does not bypass freshness, generation, one-in-flight or dispatch permission. The rolling maximum is a conservative floor based on past measurements, not a promise against the next latency spike.
Review question: Does refill_seconds=0.2 mean “run inference every 0.2 seconds”?
Answer: No. It means request when roughly 0.2 seconds of queued playback remain, unless the measured floor is larger. Request spacing depends on the chunk horizon and execution progress.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/execution.py:139 — ChunkRuntime.effective_refill
src/lerobot/inference/execution.py:191 — ChunkRuntime.should_request
tests/inference/test_aligned_execution.py:109 — test_waiting_for_playback_does_not_reserve_an_old_capture
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/execution.py:139 ChunkRuntime.effective_refill
def effective_refill(self) -> float:
"""Playback threshold including measured turnaround headroom."""
return max(self.refill_seconds, self.turnaround + self.interval)
src/lerobot/inference/execution.py:191 ChunkRuntime.should_request
def should_request(self, *, task_version: int | None = None) -> bool:
"""Check permission and playback need without reserving an observation.
Aligned task changes may bypass the playback threshold. ``begin`` still
validates their fresh capture, generation and commitment anchor.
"""
with self.lock:
self.check_deadlines()
if self.failure or not self.active or self.held or self.pending is not None:
return False
snapshot = self.queue.snapshot()
if (
self.chunk_merge == "aligned"
and task_version is not None
and self._last_anchor is not None
and task_version != self._last_anchor[2]
):
return True
if self.mode is ExecutionMode.CHUNK and self.chunk_merge == "append":
# One accepted successor beyond the executing chunk, never a chain
# of old-observation predictions hidden behind newer provenance.
sources = {p.request_id for p in snapshot.provenance if p is not None}
if len(sources) > 1:
return False
if self.current and sources and self.current.request_id not in sources:
return False
playback = self.queue.qsize() * self.interval
return playback <= self.effective_refill + 1e-9
tests/inference/test_aligned_execution.py:109 test_waiting_for_playback_does_not_reserve_an_old_capture
def test_waiting_for_playback_does_not_reserve_an_old_capture():
rt, clock = runtime(refill_seconds=0.3)
first = initial(rt, clock)
rt.pop()
clock.now += 0.1
waiting = sample(rt, clock)
assert rt.begin(waiting) is None
assert rt.pending is None
rt.pop()
clock.now += 0.1
assert rt.begin(sample(rt, clock)) is None
rt.pop()
clock.now += 0.1
latest = sample(rt, clock)
request = rt.begin(latest)
assert request is not None
assert request.observation is latest
assert request.observation.capture_time > waiting.capture_time > first.observation.capture_time
assert request.observation.action_cursor == 3
rt.pop()
assert rt.accept(request, result(request, 10), task_version=0)
assert rt.last_accept["trimmed_actions"] == 1
assert rt.pop()[0].tolist() == [11, 111]

## Slide 16
3 · READ EXECUTION
Explore request timing
Idealized aligned playback: 24 actions at 30 Hz, with 100 ms turnaround.
One prediction horizon: 24 / 30 = 0.8 seconds
Follow the trajectory
0.2 s left
0 s
0.6 s
0.8 s
Request next
Turnaround 0.10 s + one tick 0.033 s < configured refill 0.20 s
Idealized illustration: capture delay, discrete ticks and jitter change actual spacing.
At refill 0.2 s, nominal request spacing is about 0.8 − 0.2 = 0.6 s.
16
Notes: In a regular aligned cycle, the incoming prediction is anchored at capture. Its valid tail ends approximately H×Δ later. Requesting when R_effective remains therefore gives approximate request spacing H×Δ − R_effective, when that value is positive and all other gates allow it.
This approximation assumes capture near submission, regular endpoint commitment, stable turnaround and enough usable suffix. It ignores discrete tick quantization, capture delay, task changes and jitter. The interactive sliders below are explanatory arithmetic, not a runtime simulator or an automatic tuning recommendation.
If the threshold covers the whole execution horizon, playback no longer delays requests; one-in-flight and fresh-advanced-capture gates still apply. Use request_spacing_s, committed_actions_since_request and playback_at_submission_s to see what actually happened on hardware.
Review question: What changes if turnaround rises above the configured refill?
Answer: The measured floor raises the effective threshold. Requests begin earlier, reducing follow-through; a short horizon can still be insufficient.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/execution.py:220 — ChunkRuntime.begin
src/lerobot/rollout/inference/remote.py:374 — RemoteInferenceEngine._loop
tests/inference/test_aligned_execution.py:134 — test_aligned_refill_floor_uses_steady_turnaround_and_excludes_startup
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/execution.py:220 ChunkRuntime.begin
def begin(self, observation: ObservationSnapshot) -> ChunkRequest | None:
"""Reserve inference against one atomic cursor/continuation snapshot."""
with self.lock:
if not self.should_request(task_version=observation.task_version):
return None
age = self.clock() - observation.capture_time
if age < 0 or age > self.max_age:
return None # wait for a fresh capture; startup/dispatch deadlines still apply
snapshot = self.queue.snapshot()
if self.chunk_merge == "aligned":
if (
observation.execution_generation != self.generation
or observation.action_cursor is None
or observation.action_cursor > snapshot.cursor
or observation.capture_time < self.started_at
):
return None
if self._last_anchor is not None and (
(
observation.task_version == self._last_anchor[2]
and observation.action_cursor <= self._last_anchor[0]
)
or observation.capture_time <= self._last_anchor[1]
):
return None
self._last_anchor = (
observation.action_cursor,
observation.capture_time,
observation.task_version,
)
available = 0 if snapshot.model_actions is None else len(snapshot.model_actions)
self.pending = ChunkRequest(
[Excerpt continues in the source file.]
src/lerobot/rollout/inference/remote.py:374 RemoteInferenceEngine._loop
configured_refill_s=self.runtime.refill_seconds,
effective_refill_s=self.runtime.effective_refill,
scheduling="playback_threshold",
request_spacing_s=request_spacing,
committed_actions_since_request=committed_since_request,
task_changed_since_request=task_changed,
recent_turnaround_s=self.runtime.turnaround,
playback_at_submission_s=request.playback_at_submission,
observation_age_at_submission_s=request.submitted_at - observation.capture_time,
observation_cursor=observation.action_cursor,
submission_cursor=request.continuation.cursor,
)
self._last_request = (
request.generation,
request.submitted_at,
request.continuation.cursor,
observation.task_version,
)
try:
request_generation = request.generation
def request_cancelled(request_generation: int = request_generation) -> bool:
return self._stop_event.is_set() or self.runtime.generation != request_generation
result = self.client.infer(
request,
cancelled=request_cancelled,
)
except RequestCancelled:
continue
# Acceptance and an operator retarget must have one order: an
# old in-flight result cannot pass using a previously read version.
[Excerpt continues in the source file.]
tests/inference/test_aligned_execution.py:134 test_aligned_refill_floor_uses_steady_turnaround_and_excludes_startup
def test_aligned_refill_floor_uses_steady_turnaround_and_excludes_startup():
rt, clock = runtime(refill_seconds=0.01)
first = rt.begin(sample(rt, clock))
clock.now += 0.8
assert rt.accept(first, result(first), task_version=0)
assert rt.effective_refill == pytest.approx(0.1)
for _ in range(5):
rt.pop()
request = rt.begin(sample(rt, clock))
assert request is not None
clock.now += 0.25
assert rt.accept(request, result(request, 10), task_version=0)
assert rt.turnaround == pytest.approx(0.25)
assert rt.effective_refill == pytest.approx(0.35)
for _ in range(2):
rt.pop()
assert not rt.should_request() # 0.4 seconds remain
rt.pop()
assert rt.should_request() # 0.3 seconds remain: the measured floor dominates
assert rt.begin(sample(rt, clock)) is not None

## Slide 17
3 · READ EXECUTION
RTC changes the prediction itself
Plain alignment edits execution; RTC conditions inference on continuation.
Plain aligned
current observation → normal prediction → trim / replace / optional blend
No RTC model support is needed; canonical future targets are merged locally.
RTC
observation + continuation + delay → conditioned prediction → guarded
replacement
The model must implement the RTC interface and the deployment must enable that mode.
Canonical continuation preserves physical meaning; model continuation preserves model
coordinates.
17
Notes: RTC carries paired continuation spaces. For relative-action preprocessing, PolicyRunner reanchors canonical continuation against the current state and re-normalizes it instead of reusing offsets from an old observation.
Guided RTC and trained RTC are distinct capabilities. Trained RTC also has a checkpoint delay bound; the runtime rejects progress beyond what the request could condition on. RTC trimming uses its submission snapshot and timing/progress rules, not plain alignment’s capture-anchor rule.
In the current shared runtime, RTC trim is min(ceil(elapsed/Δ), cursor advance). Trained-overlap checks use the larger measured/progress bound. Plain blending is not automatically layered onto RTC. SmolVLA RTC was physically exercised; other declarations are not blanket checkpoint validation.
Review question: Would adding blend_steps give an unsupported model RTC capability?
Answer: No. Blending is a local plain-chunk merge operation. RTC requires model-side continuation conditioning.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/policy_runner.py:298 — PolicyRunner._prepare_continuation
src/lerobot/inference/execution.py:263 — ChunkRuntime.accept
src/lerobot/inference/execution.py:57 — trained_overlap_valid
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/policy_runner.py:298 PolicyRunner._prepare_continuation
def _prepare_continuation(
self, model: torch.Tensor | None, canonical: torch.Tensor | None
) -> torch.Tensor | None:
if model is None or model.numel() == 0:
return None
width = self.capabilities.action_feature.shape[0]
if model.ndim != 2 or model.shape[1] != width or not torch.isfinite(model).all():
raise ValueError("Invalid model-space continuation.")
device = self.policy.config.device or "cpu"
if self._relative_step is not None:
if canonical is None or canonical.shape != model.shape or not torch.isfinite(canonical).all():
raise ValueError("Relative RTC requires matching finite canonical continuation.")
state = self._relative_step.get_cached_state()
if state is None:
raise ValueError("Relative RTC preprocessor did not cache the current raw state.")
model = reanchor_relative_rtc_prefix(
canonical, state, self._relative_step, self._normalizer_step, device
)
horizon = self.capabilities.rtc_horizon
model = model.to(device)
if len(model) < horizon:
model = torch.cat([model, model[-1:].expand(horizon - len(model), -1)])
return model[:horizon]
src/lerobot/inference/execution.py:263 ChunkRuntime.accept
has_previous = available is not None and len(available) > 0
if self.mode is ExecutionMode.RTC_TRAINED and not trained_overlap_valid(
request.delay, max(measured, progress), self.training_max_delay, has_previous
):
return False
trim = min(measured, progress) if self.mode is not ExecutionMode.CHUNK else 0
if trim >= len(actions):
self.fault("Inference completed beyond its usable continuation horizon")
return False
provenance = replace(
chunk.provenance,
request_id=request.request_id,
generation=request.generation,
capture_time=request.observation.capture_time,
task=request.observation.task,
task_version=request.observation.task_version,
observation_id=request.observation.observation_id,
)
self.last_accept.update(
turnaround_s=elapsed,
playback_at_submission_s=request.playback_at_submission,
timing_margin_s=request.playback_at_submission - elapsed if self.has_executed else None,
cursor_advance=progress,
trimmed_actions=trim,
overlap_steps=0,
blended_steps=0,
source_age_at_acceptance_s=now - provenance.capture_time,
remaining_old_playback_s=self.queue.qsize() * self.interval,
estimated_first_dispatch_source_age_s=now
- provenance.capture_time
+ (
self.queue.qsize() * self.interval
[Excerpt continues in the source file.]
src/lerobot/inference/execution.py:57 trained_overlap_valid
def trained_overlap_valid(conditioned: int, measured: int, maximum: int, has_previous: bool) -> bool:
"""Require elapsed overlap to fit both the conditioning and training range."""
return not has_previous or measured <= min(conditioned, maximum)

## Slide 18
4 · REVIEW LIFECYCLE
Runtime deadlines and presence grace
None of these replaces sequence or generation checks.
Startup timeout
Bound the wait for the first usable action after starting/resuming.
Action request deadline
Bound a pending inference even if the worker is blocked waiting.
Maximum source age
Reject old captures and stop dispatch of actions that have become
stale.
Presence grace
Default 10 s
Release abandoned server ownership after serialized cleanup.
Fresh local timestamps do not prove that a camera delivered a new sensor frame.
18
Notes: Action/startup deadlines and source age are client-local monotonic checks. The server also times its own operations. Server durations are useful diagnostics, but cannot be subtracted directly from a client clock reading.
ObservationSnapshot.capture_time records local acquisition provenance. The present implementation does not propagate comprehensive per-camera sensor timestamps or detect every repeated-frame stall. A new wrapper read may still contain cached camera data. That limitation remains deferred.
The server’s idle_timeout_s is a presence/initial-handshake grace, currently defaulting to 10 seconds. It is not a motion recovery window: local action exhaustion or age limits can terminate the client much earlier.
Review question: If the session is still inside its presence grace, may the client execute an expired action?
Answer: No. Ownership grace and local dispatch eligibility are independent.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/execution.py:180 — ChunkRuntime.check_deadlines
src/lerobot/rollout/robot_wrapper.py:49 — ThreadSafeRobot.get_observation
src/lerobot/remote_inference/configs.py:26 — ExecutionConfig
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/execution.py:180 ChunkRuntime.check_deadlines
def check_deadlines(self) -> None:
"""Enforce local action/startup bounds even while network work is blocked."""
with self.lock:
if self.failure or not self.active or self.held:
return
now = self.clock()
if self.pending is not None and now - self.pending.submitted_at > self.action_timeout:
self.fault("Action request deadline exceeded")
elif not self.has_executed and now - self.started_at > self.startup_timeout:
self.fault("Initial action deadline exceeded")
src/lerobot/rollout/robot_wrapper.py:49 ThreadSafeRobot.get_observation
def get_observation(self) -> dict[str, Any]:
with self._lock:
sampled_at = time.monotonic()
try:
observation = self._robot.get_observation()
self._observed_positions = {
key: float(observation[key])
for key in self.action_features
if key.endswith(".pos") and key in observation
}
except Exception as exc:
self._record_hardware_failure("get_observation", exc)
raise
self._observation_time = sampled_at
return observation
src/lerobot/remote_inference/configs.py:26 ExecutionConfig
class ExecutionConfig:
"""Deployment-owned modes, timing bounds and warmup settings."""
supported_modes: list[str] = field(default_factory=lambda: ["chunk"])
action_fps: float = 30.0
rtc: RTCConfig = field(default_factory=RTCConfig)
action_deadline_s: float = 5.0
idle_timeout_s: float = 10.0
warmup_calls: int = 2
# Explicit continuous canonical coordinates; never infer gripper suitability.
blendable_components: list[str] = field(default_factory=list)

## Slide 19
4 · REVIEW LIFECYCLE
Retargeting and reset are different operations
A new instruction does not automatically mean a new session.
Retarget
set_task → task_version advances → old in-flight reply becomes ineligible
Committed motion is not rewritten. Aligned mode can request the new task before the
normal refill threshold.
Reset / planned
invalidation
revoke local motion → generation advances → serialized server control ACK
Fresh-generation action work waits for acknowledgment; a full reset also clears
model/processor state.
Invalidating motion is immediate locally; interrupting a GPU forward call is not assumed.
19
Notes: set_task updates the task and version. It does not flush every queued/committed target; they retain their original provenance. This lets execution continue until an eligible replacement arrives. The task lock gives retarget and result acceptance one order.
Runtime.invalidate increments generation, clears queued motion and the pending request, and resets local execution anchors. Remote engine controls serialize reset/invalidate requests to the server. New-generation work waits until the control acknowledgment.
PolicyRunner.reset(full=False) drops queued policy actions while preserving planner state. A full reset also resets policy and processor pairs. This distinction supports language/planner continuity without permitting old motion to leak into the resumed run.
Review question: Can reset safely run on a network callback while the model is still executing?
Answer: No. Local permission is revoked immediately, but the model reset must wait on the exclusive server worker.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/rollout/inference/remote.py:210 — RemoteInferenceEngine.set_task
src/lerobot/rollout/inference/remote.py:182 — RemoteInferenceEngine._invalidate
tests/remote_inference/test_session.py:175 — test_reset_acknowledges_only_after_current_model_call_and_reset
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/rollout/inference/remote.py:210 RemoteInferenceEngine.set_task
def set_task(self, task: str) -> bool:
if len(task) > self.client.descriptor["limits"]["max_input_chars"]:
raise ValueError("Instruction exceeds deployed text limit")
changed = super().set_task(task)
if changed:
self._event("task", task=task, task_version=self.task_version)
return changed
src/lerobot/rollout/inference/remote.py:182 RemoteInferenceEngine._invalidate
def _invalidate(self, operation: str) -> None:
with self._lock:
generation = self.runtime.invalidate()
self._observation = None
self._hold_requested = False
self._hold_acknowledged = False
# A later motion invalidation must not erase a pending full reset.
if self._control is not None and self._control[0] == "reset":
operation = "reset"
self._control = (operation, generation)
self._event(operation)
tests/remote_inference/test_session.py:175 test_reset_acknowledges_only_after_current_model_call_and_reset
def test_reset_acknowledges_only_after_current_model_call_and_reset(worker):
session = admit(worker)
entered, release = block_predict(worker)
try:
action = worker.submit(action_request(worker, session))
assert entered.wait(2)
reset_request = control_request(worker, session, 1, "reset")
reset = worker.submit(reset_request)
assert worker.submit(reset_request) is reset
assert not reset.done()
assert worker.runner.policy.resets == 2
assert_error(worker.submit(action_request(worker, session, generation=1)).result(2), ErrorCode.STALE)
release.set()
assert action.result(2).message_type is MessageType.ACTION
assert reset.result(2).body["applied_generation"] == 1
assert worker.runner.policy.resets == 3
assert_error(worker.submit(action_request(worker, session)).result(2), ErrorCode.STALE)
assert (
worker.submit(action_request(worker, session, generation=1)).result(2).message_type
is MessageType.ACTION
)
finally:
release.set()

## Slide 20
4 · REVIEW LIFECYCLE
Session cleanup preserves model ownership
A disappeared process cannot be replaced while its model call is still mutating state.
Admitted
initial presence
then active ownership
→
Absent
grace countdown
restoration can cancel
→
Closing
stop accepting data
queue cleanup
→
Released
current call finishes
full reset completes
Grace expiry schedules cleanup; it does not forcibly free a busy model.
20
Notes: SessionWorker distinguishes waiting for initial presence from a later disconnect. This removed the misleading admitted/absent/restored log pattern at every normal connection.
Server-side cleanup can be cancelled if client presence returns within grace before closing begins. This does not restore client inference permission: RemoteClient.present latches any observed server-token loss, so returning server presence cannot enable new requests. Valid buffered motion may drain until local limits stop it. A fresh client process is a new owner and does not adopt the old session.
Clean close releases ownership after worker cleanup. Abrupt disappearance waits the grace and then follows the same serialized cleanup path. A hung model call still owns its state after grace; admitting another client at that point would violate isolation. There is no automatic motion recovery after a terminal fault.
Review question: Should a new client succeed exactly 10 seconds after killing the old one?
Answer: Not necessarily. Presence detection, queueing and the current model call/reset must finish. The grace is not a guaranteed re-admission deadline.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/remote_inference/server.py:604 — SessionWorker.expire
src/lerobot/remote_inference/server.py:432 — SessionWorker._execute
tests/remote_inference/test_session.py:355 — test_absence_cleanup_never_reuses_a_blocked_model_after_grace
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/remote_inference/server.py:604 SessionWorker.expire
def expire(self, *, present: bool) -> None:
"""Bound initial presence and later absence; release only through the worker."""
with self._lock:
session = self._session
if session is None or session.closing:
return
now = time.monotonic()
if present:
if not session.presence_established:
logger.info(
"Session initial presence established instance=%s session=%s",
self.instance_id,
session.identity,
)
elif session.present is False:
logger.info(
"Session presence restored instance=%s session=%s; absence cleanup cancelled",
self.instance_id,
session.identity,
)
session.present = True
session.presence_established = True
session.absent_since = None
session.cleanup_queue_blocked = False
return
session.present = False
if session.absent_since is None:
session.absent_since = now
logger.info(
(
"Session client absent instance=%s session=%s grace_s=%.3f inference_pending=%s"
if session.presence_established
[Excerpt continues in the source file.]
src/lerobot/remote_inference/server.py:432 SessionWorker._execute
def _execute(self, message: Envelope) -> Envelope:
session = self._session
if session is None:
return message.error(ErrorCode.STALE, "Session closed")
if message.message_type is not MessageType.OPEN and message.session_id != session.identity:
return message.error(ErrorCode.STALE, "Session ownership changed before execution")
if message.message_type is MessageType.OPEN:
self.runner.reset(full=True)
session.ready = True
logger.info("Session admitted instance=%s session=%s", self.instance_id, session.identity)
return Envelope(
MessageType.ACCEPTED,
self.instance_id,
session.identity,
0,
message.request_id,
{**self.descriptor, "mode": session.mode.value, "chunk_settings": session.chunk_settings},
)
if message.message_type is MessageType.CONTROL:
operation = message.body["operation"]
if operation != "close" and message.generation < session.generation:
return message.error(ErrorCode.STALE, "Control generation became obsolete while queued")
if operation == "status" and message.generation != session.generation:
return message.error(ErrorCode.STALE, "Status generation does not match")
if operation == "close" or (
operation in {"reset", "invalidate"} and message.generation > session.generation
):
self.runner.reset(full=operation != "invalidate")
session.generation = message.generation
response = message.reply(
MessageType.ACK, {"operation": operation, "applied_generation": session.generation}
)
[Excerpt continues in the source file.]
tests/remote_inference/test_session.py:355 test_absence_cleanup_never_reuses_a_blocked_model_after_grace
def test_absence_cleanup_never_reuses_a_blocked_model_after_grace(worker, cleanup_clock):
session = admit(worker)
worker.expire(present=True)
entered, release = block_predict(worker)
try:
action = worker.submit(action_request(worker, session))
assert entered.wait(2)
worker.expire(present=False)
cleanup_clock[0] += 10
worker.expire(present=False)
state = worker.descriptor["session"]
assert state["owner"] == session
assert state["absence_grace_remaining_s"] == 0.0
assert state["cleanup_reason"] == "client_absence"
assert state["admission_blocker"] == "unfinished_inference"
# Neither additional absence nor a late presence token revokes an ordered close.
cleanup_clock[0] += 300
worker.expire(present=False)
worker.expire(present=True)
assert_error(worker.submit(open_request(worker)).result(2), ErrorCode.BUSY)
assert worker.runner.policy.resets == 2
after_cleanup = worker.submit(control_request(worker, session, 0, "status"))
assert not after_cleanup.done()
release.set()
assert_error(action.result(2), ErrorCode.TIMEOUT)
assert_error(after_cleanup.result(2), ErrorCode.STALE)
assert admit(worker) != session
finally:
[Excerpt continues in the source file.]

## Slide 21
4 · REVIEW LIFECYCLE
Terminal fault becomes local shutdown
The robot can return to its initial pose even when the server is gone.
Fault latch
deadline / age
or action exhaustion
→
Revoke motion
clear future
reset interpolation
→
Local cleanup
hold attempt → stop
engine
configured return
→
Disconnect
robot driver applies
its torque behavior
Return requires enabled configuration, a captured initial pose and no known hardware I/O failure.
21
Notes: ChunkRuntime.fault invalidates motion and latches failure. Later reset/invalidate cannot clear that terminal latch. The engine reports the fault. It lets the control thread issue a local hold before acknowledge_hold signals global shutdown; then the controller ends the segment and runs teardown.
Teardown clears interpolation, attempts a local hold when appropriate, stops the engine, then honors return_to_initial_position when its prerequisites hold. A known robot read/send/hold failure suppresses further shutdown movement. Returning uses local hardware and does not need the server.
Disconnect may remove torque according to the driver configuration. A transient hold command is not a promise of indefinite pose retention. The focused hardware test passed after the revised return behavior; broader hardware teardown hardening remains a separate concern.
Review question: Does restarting the server restore motion after Active motion buffer exhausted?
Answer: No. The client has latched a terminal fault and is shutting down. A later run needs a new client/session.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/execution.py:172 — ChunkRuntime.fault
src/lerobot/rollout/strategies/core.py:227 — RolloutStrategy._teardown_hardware
tests/test_remote_rollout.py:298 — test_terminal_fault_shutdown_orders_hold_stop_home_disconnect
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/execution.py:172 ChunkRuntime.fault
def fault(self, reason: str) -> None:
"""Latch a terminal fault; invalidate does not clear this latch."""
with self.lock:
if self.failure is None:
self.failure = reason
self.invalidate(held=True)
self.active = False
src/lerobot/rollout/strategies/core.py:227 RolloutStrategy._teardown_hardware
def _teardown_hardware(self, hw: HardwareContext, return_to_initial_position: bool = True) -> None:
"""End policy execution, perform configured local shutdown movement, and disconnect.
A terminal inference fault does not imply failed local hardware. Honor
the return setting in that case; never home through a known I/O failure.
Disconnect torque behavior belongs to the robot driver, not the hold.
"""
wrapper = hw.robot_wrapper
if self._interpolator is not None:
self._interpolator.reset()
self._cached_obs_processed = None
try:
if self._engine is not None:
logger.info("Stopping inference engine...")
if self._engine.failed and wrapper.supports_hold and wrapper.hardware_failure is None:
try:
wrapper.hold()
except Exception:
logger.exception("Fault hold failed; skipping further shutdown movement")
self._engine.stop()
finally:
robot = wrapper.inner
try:
if robot.is_connected:
try:
if wrapper.hardware_failure is not None:
logger.warning(
"Skipping return-to-initial-position: robot I/O failed: %s",
wrapper.hardware_failure,
)
elif not return_to_initial_position:
logger.info("Skipping return-to-initial-position: disabled by config")
[Excerpt continues in the source file.]
tests/test_remote_rollout.py:298 test_terminal_fault_shutdown_orders_hold_stop_home_disconnect
def test_terminal_fault_shutdown_orders_hold_stop_home_disconnect(monkeypatch):
engine = GateEngine()
engine.failed = True
ctx, robot = make_dispatch_context(engine)
strategy = BaseStrategy(BaseStrategyConfig())
strategy._engine = engine
strategy._interpolator = ActionInterpolator()
strategy._interpolator.add(torch.tensor([123.0]))
strategy._cached_obs_processed = {"joint.pos": 123.0}
events = []
monkeypatch.setattr(robot, "send_action", lambda action: events.append(("action", action.copy())))
monkeypatch.setattr(engine, "stop", lambda: events.append(("engine_stop", None)))
monkeypatch.setattr(robot, "disconnect", lambda: events.append(("disconnect", None)))
monkeypatch.setattr("lerobot.rollout.strategies.core.precise_sleep", lambda _: None)
strategy._teardown_hardware(ctx.hardware)
assert events[0] == ("action", {"joint.pos": 7.0})
assert events[1] == ("engine_stop", None)
assert events[-2] == ("action", {"joint.pos": 0.0})
assert events[-1] == ("disconnect", None)
assert strategy._interpolator.get() is None
assert strategy._cached_obs_processed is None

## Slide 22
4 · REVIEW LIFECYCLE
Language is a planned hold path
Text work shares the policy worker, so motion is explicitly suspended.
Request query
revoke motion
advance generation
→
Motor ACK
clear interpolation
hold command issued
→
Text operation
fresh held capture
isolated processors
→
Resume
validate answer
context
new action capture
Implemented and software-tested; real text-capable checkpoint acceptance is still deferred.
22
Notes: The acknowledgment means the local hold command was issued, not that sensors proved physical stillness. The control thread must acknowledge the hold before the worker sends the generation control and language request. The query requires a new capture after the control thread acknowledges issuing the hold. The worker receives the server generation-control acknowledgment before submitting language work. A queued full reset must not be downgraded by a later hold request.
PolicyRunner uses an isolated language processor pair, while the policy is still accessed through the same serialized worker. Query IDs, task versions and autosteering intent prevent obsolete answers from changing the current task.
After language work completes without a terminal fault, the old observation is discarded so action inference receives a post-query capture. A recoverable text/execution error can return an error answer and resume; timeout or uncertain protocol state faults the rollout. Autosteering requires a real dispatched action after applying a subtask before another subtask query. Natural-language task conditioning alone does not mean a policy implements VQA.
Review question: Why not let the robot finish a long chunk while a slow VQA call runs?
Answer: The agreed behavior is a planned local hold, with bounded serialized language work and fresh resumption. Concurrent action/text scheduling is outside this implementation.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/rollout/inference/remote.py:282 — RemoteInferenceEngine._request_language_hold
src/lerobot/rollout/inference/remote.py:374 — RemoteInferenceEngine._loop
tests/remote_inference/test_engine.py:159 — test_query_waits_for_hold_acknowledgment_and_new_capture
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/rollout/inference/remote.py:282 RemoteInferenceEngine._request_language_hold
def _request_language_hold(self) -> None:
with self._lock:
if not self.runtime.active or self._hold_requested or self.failed:
return
generation = self.runtime.invalidate(held=True)
self._hold_requested = True
self._hold_acknowledged = False
self._hold_started = time.monotonic()
self._observation = None
operation = "reset" if self._control is not None and self._control[0] == "reset" else "invalidate"
self._control = (operation, generation)
self._event("planned_hold")
src/lerobot/rollout/inference/remote.py:374 RemoteInferenceEngine._loop
continue
if hold_ready:
with self._lock:
# Reset/pause may arrive after the initial loop snapshot.
# A new-generation query must wait for its ordered control
# acknowledgement, just like an action request.
eligible = (
self._control is None
and self.runtime.active
and self._hold_requested
and self._hold_acknowledged
and observation is self._observation
and observation.capture_time >= self._hold_started
)
generation = self.runtime.generation
if eligible:
self._query_observation, self._query_generation = observation, generation
if not eligible:
self._stop_event.wait(0.002)
continue
self._service_query({})
with self._lock:
if self.runtime.generation == generation and not self.failed:
self.runtime.held = False
self.runtime.started_at = time.monotonic()
self._hold_requested = False
self._hold_acknowledged = False
self._observation = None # action always gets a post-query capture
continue
if self.has_pending_query or not self.client.present:
self.runtime.check_deadlines()
self._stop_event.wait(0.002)
[Excerpt continues in the source file.]
tests/remote_inference/test_engine.py:159 test_query_waits_for_hold_acknowledgment_and_new_capture
def test_query_waits_for_hold_acknowledgment_and_new_capture(session):
engine, client = session
engine.resume()
capture(engine)
assert engine.ask("What is visible?")
engine.start()
assert not client.control_started.wait(0.02)
assert not client.text_started.is_set()
assert not engine.dispatch_allowed()
engine.acknowledge_hold()
assert client.control_started.wait(2)
assert not client.text_started.wait(0.02), "the pre-hold capture cannot condition text"
capture(engine)
assert client.text_started.wait(2)
client.text_release.set()
assert wait_for(lambda: bool(engine._ready_answers))
delivered = []
engine.set_answer_observer(delivered.append)
assert delivered == []
engine.pump_query()
assert delivered[0].answer == "an answer"
assert not client.action_started.is_set(), "action resumption requires another fresh capture"
capture(engine)
assert client.action_started.wait(2)
assert client.max_active_calls == 1

## Slide 23
5 · PREPARE YOUR REVIEW
Policy compatibility is an execution contract
A small declaration is appropriate only when it describes the policy truthfully.
ACT
Default direct-chunk contract; temporal ensembling must be disabled.
SmolVLA / XVLA
Targeted input validation preserves existing resize, masks and state
preparation.
LaWAM
Declares its returned action horizon and current-only inference
preparation.
History-dependent policies
Need real observation / executed-action semantics; bypassing guards
is insufficient.
The policy audit separates source-compatible candidates from physically exercised checkpoints.
23
Notes: chunk_inference_spec declares prediction/execution lengths and available modes. validate_chunk_input_features distinguishes accepted canonical inputs from the checkpoint’s existing preparation. The exact negotiated wire schema remains strict.
The inherited contract rejects history and certain stateful preparation patterns it cannot represent. LingBot, for example, consumes frame/executed-action history and model cache state; constant-width current snapshots are not enough. Some other policies only need a targeted horizon declaration.
Read policy_support_audit.md for all 21 built-in families and their caveats. The runner currently uses direct construction, not a generic YAML adapter registry. An extension should solve a concrete checkpoint need without weakening the guarantees for existing ones.
Review question: Is “remove the history validation check” a complete adapter?
Answer: No. It removes the failure signal without supplying the history and execution feedback the model actually needs.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/policies/pretrained.py:307 — PreTrainedPolicy.chunk_inference_spec
src/lerobot/policies/lawam/modeling_lawam.py:221 — LaWAMPolicy.chunk_inference_spec
src/lerobot/policies/smolvla/modeling_smolvla.py:338 — SmolVLAPolicy.validate_chunk_input_features
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/policies/pretrained.py:307 PreTrainedPolicy.chunk_inference_spec
def chunk_inference_spec(self) -> ChunkPolicySpec:
"""Declare the default current-observation chunk-serving author contract.
Inheriting this implementation declares that ``predict_action_chunk`` does
every preparation needed by direct callers, accepts the complete current
observation, and returns ``[B, chunk_size, A]`` in model coordinates. Its
canonical processor pair must support whole chunks. ``n_action_steps`` is
the ordinary playback slice; RTC retains the full prediction horizon.
A policy requiring select_action-only preparation, other action layouts,
or temporal sampling must override this method and reject unsupported
configurations or provide a custom runner. Method presence or a successful
warmup is not evidence for this contract. Policy/processor state is allowed
only within an exclusive session and reset() must clear it for a new run.
"""
config = self.config
if config.n_obs_steps != 1:
raise ValueError("Chunk serving requires n_obs_steps=1; observation history is unsupported.")
for field_name in (
"observation_delta_indices",
"image_observation_delta_indices",
"state_observation_delta_indices",
):
indices = getattr(config, field_name, None)
if indices is not None and list(indices) != [0]:
raise ValueError(f"Chunk serving cannot sample temporal history ({field_name}).")
if getattr(config, "temporal_ensemble_coeff", None) is not None:
raise ValueError("Chunk serving does not support temporal ensembling.")
if getattr(config, "use_visual_memory", False) or getattr(config, "use_proprioceptive_memory", False):
raise ValueError(
"Chunk serving cannot sample observation memory at the required control cadence."
)
[Excerpt continues in the source file.]
src/lerobot/policies/lawam/modeling_lawam.py:221 LaWAMPolicy.chunk_inference_spec
def chunk_inference_spec(self) -> ChunkPolicySpec:
"""Serve current observations and the wrapper's already-cropped action horizon.
Future image indices are training targets for the LAM teacher. Inference
predicts the future representation from the current images instead.
"""
if self.config.n_obs_steps != 1:
raise ValueError("LaWAM chunk serving requires n_obs_steps=1.")
return ChunkPolicySpec(
prediction_steps=self.config.action_horizon,
execution_steps=self.config.n_action_steps,
)
src/lerobot/policies/smolvla/modeling_smolvla.py:338 SmolVLAPolicy.validate_chunk_input_features
def validate_chunk_input_features(self, features: tuple[FeatureSpec, ...]) -> None:
"""Preserve prepare_images' camera subset, resizing and padding semantics.
The deployment explicitly selects physical cameras. Missing visual slots
remain missing; prepare_images applies the checkpoint's empty-camera limit
and masks exactly as in local inference. Never synthesize unmasked cameras.
"""
expected = self.config.input_features or {}
supplied = {feature.name: feature for feature in features}
required = {name for name, feature in expected.items() if feature.type != FeatureType.VISUAL}
if not required <= supplied.keys() or not supplied.keys() <= expected.keys():
raise ValueError("SmolVLA requires all nonvisual inputs and only known camera features.")
if not any(expected[name].type == FeatureType.VISUAL for name in supplied):
raise ValueError("SmolVLA requires at least one camera.")
for name, feature in supplied.items():
policy_feature = expected[name]
if policy_feature.type == FeatureType.VISUAL:
shape = policy_feature.shape
if len(shape) != 3 or shape[0] != 3 or feature.kind != "rgb":
raise ValueError(f"SmolVLA requires RGB camera inputs: {name}.")
if self.config.resize_imgs_with_padding is None and feature.shape != (
shape[1],
shape[2],
shape[0],
):
raise ValueError(f"RGB feature shape differs without policy resizing: {name}.")
elif feature.kind != "tensor" or feature.shape != tuple(policy_feature.shape):
raise ValueError(f"Tensor feature shape differs from checkpoint: {name}.")

## Slide 24
5 · PREPARE YOUR REVIEW
Read logs as a causal chain
Match request identity and control ticks before attributing a visible bump.
request
playback at
submission
capture age + spacing
→
result
turnaround + worker
time
trim / overlap / blend
→
first_dispatch
source age
transition delta
→
dispatch
canonical →
command
measured state
Server policy time is only one part of client turnaround.
24
Notes: Use configured_refill_s versus effective_refill_s to see whether the measured floor dominates. Compare playback_at_submission_s with turnaround_s for margin, then inspect accepted status, usable suffix and source age.
A result log can show low network/compute delay while append still delays first dispatch behind old playback. Alignment can reduce that wait while introducing a trajectory discontinuity. transition_delta and replacement_delta help locate the boundary, but do not independently prove the cause of a physical bump.
When dataset recording is configured, the bounded asynchronous JSONL sidecar records request/result/dispatch provenance. Canonical values, robot-processed commands and measured scalar positions remain distinct. first_dispatch is captured at the first queue pop for a request: endpoint commitment, not confirmed hardware arrival or send. dispatch records the send path. The bounded sidecar can drop overflowing telemetry, reported at writer close. Source/video correlation needs actual timing; coarse logs alone cannot prove an exact physical cause.
Review question: A server forward takes 100 ms. Is that the latency value used by refill?
Answer: No. The runtime measures complete client turnaround, including transport, server work and response handling. Its steady rolling maximum feeds the refill floor.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/rollout/inference/remote.py:374 — RemoteInferenceEngine._loop
src/lerobot/rollout/inference/remote.py:527 — RemoteInferenceEngine.record_dispatch
src/lerobot/inference/execution.py:445 — ChunkRuntime.pop
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/rollout/inference/remote.py:374 RemoteInferenceEngine._loop
capture_time=observation.capture_time,
task_version=observation.task_version,
delay=request.delay,
chunk_merge=self.config.chunk_merge,
configured_refill_s=self.runtime.refill_seconds,
effective_refill_s=self.runtime.effective_refill,
scheduling="playback_threshold",
request_spacing_s=request_spacing,
committed_actions_since_request=committed_since_request,
task_changed_since_request=task_changed,
recent_turnaround_s=self.runtime.turnaround,
playback_at_submission_s=request.playback_at_submission,
observation_age_at_submission_s=request.submitted_at - observation.capture_time,
observation_cursor=observation.action_cursor,
submission_cursor=request.continuation.cursor,
)
self._last_request = (
request.generation,
request.submitted_at,
request.continuation.cursor,
observation.task_version,
)
try:
request_generation = request.generation
def request_cancelled(request_generation: int = request_generation) -> bool:
return self._stop_event.is_set() or self.runtime.generation != request_generation
result = self.client.infer(
request,
cancelled=request_cancelled,
)
[Excerpt continues in the source file.]
src/lerobot/rollout/inference/remote.py:527 RemoteInferenceEngine.record_dispatch
def record_dispatch(self, canonical: dict, command: dict, measured: dict) -> None:
super().record_dispatch(canonical, command, measured)
provenance = self.runtime.current
if provenance is None:
return
scalar_state = {
key: float(value)
for key, value in measured.items()
if isinstance(value, (float, int, np.number)) and np.isfinite(value)
}
self._event(
"dispatch",
provenance=asdict(provenance),
canonical=canonical,
command=command,
measured=scalar_state,
source_age_s=time.monotonic() - provenance.capture_time,
)
src/lerobot/inference/execution.py:445 ChunkRuntime.pop
def pop(self, *, control_tick: int | None = None) -> tuple[torch.Tensor, ActionProvenance] | None:
"""Commit an endpoint to interpolation; its provenance remains age-checked."""
with self.lock:
if not self.dispatch_allowed():
return None
item = self.queue.get_with_provenance()
if item is None:
if self.has_executed:
self.fault("Active motion buffer exhausted")
return None
action, _, provenance = item
if provenance is None:
self.fault("Action lacks request provenance")
return None
self.current = provenance
self.has_executed = True
if not self.dispatch_allowed():
return None
if provenance.request_id != self._last_dispatch_request:
self._last_dispatch_request = provenance.request_id
self.dispatch_events.append(
{
"time": self.clock(),
"generation": provenance.generation,
**({"control_tick": control_tick} if control_tick is not None else {}),
"request_id": provenance.request_id,
"source_age_s": self.clock() - provenance.capture_time,
"contributor_count": provenance.contributor_count,
"action_cursor": self.queue.snapshot().cursor,
"transition_delta": None
if self._last_action is None
else (action - self._last_action).tolist(),
[Excerpt continues in the source file.]

## Slide 25
5 · PREPARE YOUR REVIEW
Tests encode the important counterexamples
Read the test first when an ordering guarantee feels abstract.
execution /
aligned_execution
Capture before submission, committed trimming, timing gates, oldest
blend age.
remote_inference / session
+ engine
Duplicate requests, blocked resets, presence cleanup, retarget and
language races.
test_remote_rollout
Interpolation revocation and hold → stop → return → disconnect
ordering.
remote path / codec /
transport
Checkpoint boundary, malformed payloads and actual process/Zenoh
exchange.
Software tests establish bounded cases. Hardware reports establish observed task and motion
behavior.
25
Notes: Start with test_observation_anchor_accounts_for_progress_before_and_during_request: a tiny clock advance demonstrates that plain alignment uses cursor progress, including before submission. Then read the test proving refill waits without reserving an old capture.
For lifecycle, read the blocked-reset and blocked-absence tests: they make model ownership visible by pausing a policy call. For the robot path, read the test that revokes permission during a pull and the test checking terminal shutdown order.
The source excerpts here are documentation evidence; creating this learning guide does not imply those runtime tests were rerun today. Controlled model/robot tests do not replace a real language checkpoint or a representative WAN experiment.
Review question: Which counterexample should fail if alignment accidentally switches to elapsed-time trimming?
Answer: A capture followed by multiple cursor commitments but only a tiny clock advance. The existing anchor test covers exactly that distinction.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
tests/inference/test_aligned_execution.py:59 — test_observation_anchor_accounts_for_progress_before_and_during_request
tests/remote_inference/test_session.py:175 — test_reset_acknowledges_only_after_current_model_call_and_reset
tests/test_remote_rollout.py:117 — test_permission_revoked_during_pull_cannot_dispatch_returned_action
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
tests/inference/test_aligned_execution.py:59 test_observation_anchor_accounts_for_progress_before_and_during_request
def test_observation_anchor_accounts_for_progress_before_and_during_request():
rt, clock = runtime()
initial(rt, clock)
rt.pop() # committed endpoint 0, still potentially interpolating toward it
clock.now += 0.1
source = sample(rt, clock) # action zero assigned to endpoint 1
rt.pop() # endpoint 1 committed before request submission
request = rt.begin(source)
assert request.continuation.cursor == 2
rt.pop() # endpoint 2 committed during inference
clock.now += 0.001 # wall-time estimate is irrelevant to aligned trimming
assert rt.accept(request, result(request, 10), task_version=0)
assert rt.last_accept["trimmed_actions"] == 2
assert rt.queue.qsize() == 4
assert rt.pop()[0].tolist() == [12, 112]
tests/remote_inference/test_session.py:175 test_reset_acknowledges_only_after_current_model_call_and_reset
def test_reset_acknowledges_only_after_current_model_call_and_reset(worker):
session = admit(worker)
entered, release = block_predict(worker)
try:
action = worker.submit(action_request(worker, session))
assert entered.wait(2)
reset_request = control_request(worker, session, 1, "reset")
reset = worker.submit(reset_request)
assert worker.submit(reset_request) is reset
assert not reset.done()
assert worker.runner.policy.resets == 2
assert_error(worker.submit(action_request(worker, session, generation=1)).result(2), ErrorCode.STALE)
release.set()
assert action.result(2).message_type is MessageType.ACTION
assert reset.result(2).body["applied_generation"] == 1
assert worker.runner.policy.resets == 3
assert_error(worker.submit(action_request(worker, session)).result(2), ErrorCode.STALE)
assert (
worker.submit(action_request(worker, session, generation=1)).result(2).message_type
is MessageType.ACTION
)
finally:
release.set()
tests/test_remote_rollout.py:117 test_permission_revoked_during_pull_cannot_dispatch_returned_action
def test_permission_revoked_during_pull_cannot_dispatch_returned_action():
engine = GateEngine()
engine.stop_during_pull = True
ctx, robot = make_dispatch_context(engine)
assert send_next_action({"joint.pos": 7.0}, {}, ctx, ActionInterpolator()) is None
assert robot.sent == [{"joint.pos": 7.0}]

## Slide 26
5 · PREPARE YOUR REVIEW
A focused first code review
Follow one guarantee all the way through its implementation and test.
Pass 1
Types +
execution
contracts.py →
ChunkRuntime →
ActionQueue
Pass 2
One real request
RemoteInferenceEngine
→ RemoteClient →
SessionWorker →
PolicyRunner
Pass 3
Revoke
permission
reset / hold / fault →
interpolation gate →
teardown
Pass 4
Try to break a
guarantee
Retarget during
inference; reset during
a blocked model call
Ask: who owns this state, what makes it stale, and which test proves the boundary?
26
Notes: For the first review session, choose plain aligned ACT and ignore optional language/RTC internals until you can trace capture → request → merge → dispatch. Keep the policy execution slice separate from the prediction horizon throughout.
For each mutation, note the thread, lock and identity it depends on. For each cached value, ask whether its source timestamp and generation survive. For each callback, check whether it can block or mutate policy state.
Useful review targets are concrete: acceptance racing with task changes; snapshot consistency; a result arriving after invalidation; a blended action nearing its oldest-source age bound; hardware cleanup after a terminal remote fault. Future multi-client serving, cloud packaging and MPC are not prerequisites for reviewing this implementation.
Review question: Can you explain the guarantee behind runtime.pending is request?
Answer: It binds acceptance to the exact locally reserved request. A response for a canceled/replaced reservation cannot refill motion merely because some IDs or timestamps look plausible.
Sources at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/execution.py:263 — ChunkRuntime.accept
src/lerobot/rollout/inference/remote.py:374 — RemoteInferenceEngine._loop
src/lerobot/rollout/strategies/core.py:443 — send_next_action
Source excerpts at c73a3f0403046f669326ca896755b00cbef415fa:
src/lerobot/inference/execution.py:263 ChunkRuntime.accept
def accept(self, request: ChunkRequest, chunk: ActionChunk, *, task_version: int) -> bool:
"""Validate context and timing, then atomically merge with original provenance."""
with self.lock:
self.last_accept = {"accepted": False}
self.check_deadlines()
if self.failure or self.pending is not request or request.generation != self.generation:
return False
self.pending = None
if request.observation.task_version != task_version:
return False
now = self.clock()
elapsed = now - request.submitted_at
self._completed += 1
if self._completed > 1: # cold start is not a steady-state action latency
self.turnarounds.append(elapsed)
if now - request.observation.capture_time > self.max_age:
self.fault("Action result source observation is too old")
return False
actions = chunk.canonical_actions
model = chunk.model_actions if chunk.model_actions is not None else actions
if (
actions.ndim != 2
or model.ndim != 2
or len(actions) != len(model)
or not len(actions)
or type(chunk.execution_steps) is not int
or not 0 < chunk.execution_steps <= len(actions)
or not torch.isfinite(actions).all()
or not torch.isfinite(model).all()
):
self.fault("Invalid action chunk")
return False
[Excerpt continues in the source file.]
src/lerobot/rollout/inference/remote.py:374 RemoteInferenceEngine._loop
continue
# Acceptance and an operator retarget must have one order: an
# old in-flight result cannot pass using a previously read version.
with self._task_lock:
accepted = self.runtime.accept(request, result, task_version=self._task_version)
self._warn_refill_horizon()
self._event(
"result",
request_id=request.request_id,
accepted=accepted,
turnaround_s=time.monotonic() - request.submitted_at,
source_age_s=time.monotonic() - observation.capture_time,
queue_playback_s=self.runtime.queue.qsize() * self.runtime.interval,
server_durations=result.server_durations,
merge=self.runtime.last_accept.copy(),
)
except Exception as exc:
self._traceback = traceback.format_exc()
self._fault(str(exc))
logger.exception("Remote inference worker fault")
finally:
if self.runtime.failure is not None:
self._fault(self.runtime.failure)
try:
self.client.close()
except Exception:
logger.exception("Remote session close failed; presence/idle cleanup will release it")
src/lerobot/rollout/strategies/core.py:443 send_next_action
def send_next_action(
obs_processed: dict,
obs_raw: dict,
ctx: RolloutContext,
interpolator: ActionInterpolator,
timer: CycleTimer | None = None,
) -> dict | None:
"""Dispatch the next action to the robot.
Pulls the next action tensor from the inference engine, feeds the
interpolator, and sends the interpolated action through the
``robot_action_processor`` to the robot. Works identically for
sync and async backends — the rollout strategy never needs to branch.
When *timer* is given, the engine pull and the robot send are timed as the
``infer`` and ``send`` steps of its cadence summary, and a tick with no action
to send is counted there. Note that on async backends ``infer`` is only a
queue pull — inference runs off-thread, so its latency surfaces as starved
ticks rather than as loop-body time.
Returns the action dict that was sent, or ``None`` if no action was
ready (e.g. empty async queue, interpolator not yet primed).
"""
engine = ctx.policy.inference
engine.begin_control_tick()
features = ctx.data.dataset_features
ordered_keys = ctx.data.ordered_action_keys
# ``nullcontext`` accepts (and ignores) the section name, so it stands in for
# ``timer.section`` verbatim when no timer was passed.
section = timer.section if timer is not None else contextlib.nullcontext
def dispatch_permitted() -> bool:
[Excerpt continues in the source file.]