## Slide 1
Async remote inference
01
A visual walkthrough
of the system we built
LeRobot
Experience, motion, then code
Implementation snapshot: 29 September 2026
Notes: This walkthrough explains the implementation in this checkout on 2026-09-29. Read it in three passes: the operator experience, chunk behavior, then code. The recent refill correction is a design decision only and has not been implemented. The photograph comes from your successful ACT baseline video. The browser version offers optional notes, source links and short questions. PowerPoint retains editable diagrams and speaker notes.
Sources in repository (snapshot 2026-09-29):
remote_inference_docs/async_proposal.md
remote_inference_docs/implementation_progress.md
test1-client.mp4

## Slide 2
Two processes, one robot task
02
Robot host
172.18.133.214
GPU server
172.18.131.152
observation
Buffered actions
Policy prediction
action chunk
Cameras, motor commands, operator
Weights, processors, GPU
The same separation also works between two processes on one computer.
Notes: The robot host owns cameras, motor access, operator interaction and rollout recording. The server owns one preloaded policy, its policy processors and GPU computation. The client does not load model weights. The current deployment admits one active robot session. Both processes can also run on the same host. Separating them keeps model execution out of the motor control loop, but network and inference delays still need a usable action buffer.
Sources in repository (snapshot 2026-09-29):
src/lerobot/rollout/remote_context.py:50
src/lerobot/scripts/lerobot_policy_server.py:65
src/lerobot/remote_inference/server.py:77

## Slide 3
What the operator experiences
03
Server ready
Client admitted
First result
Robot moves
Policy warmup
Contract checks
Startup waiting
Local dispatch
Interactive mode adds an explicit /start before motion.
A fault ends motion permission. Reconnecting does not automatically resume a rollout.
Notes: Start the server and wait for its deployment to warm and become ready. A client discovers the descriptor and checks feature/action contracts, execution support and position-hold capability before policy motion. Hardware can connect during setup, so admission is a before-policy-motion guarantee rather than a promise of no hardware connection. Non-interactive base rollout begins after startup. Interactive rollout waits for /start. Normal completion may return to the initial pose according to rollout configuration. A terminal inference fault instead holds and suppresses normal homing. A dead client cannot execute a software hold.
Sources in repository (snapshot 2026-09-29):
src/lerobot/scripts/lerobot_policy_server.py:140
src/lerobot/rollout/remote_context.py:50
src/lerobot/rollout/strategies/core.py:222

## Slide 4
The two commands have different jobs
04
Server
lerobot-policy-server
--config_path=…/omx_act_lan.yaml
--model.repo_or_path=
maximellerbach/omx_pickandplace_act
Selects and loads the model
Client
lerobot-rollout
--inference.type=remote
--inference.deployment=omx-act
--inference.chunk_merge=append
--inference.refill_seconds=0.1
Owns robot and camera settings
Excerpts only. Endpoint, semantics, hold mode and hardware arguments are also required.
Notes: These are configuration excerpts, not complete hardware commands. On the server use uv run --no-sync lerobot-policy-server --config_path=examples/remote_inference/omx_act_lan.yaml --model.repo_or_path=maximellerbach/omx_pickandplace_act. The preset already binds tcp/172.18.131.152:7447, uses deployment omx-act, CUDA, chunk mode, action_fps 30 and a 30-second absence grace. On the robot host use lerobot-rollout with inference.type=remote, endpoint, deployment, mode, semantics and hold_mode. Add the actual robot, camera, task, fps and duration settings from your validated setup. Do not pass a local policy.path or device to remote rollout. The latest logs used camera indices 1 and 4, so the workbook camera indices should not be copied blindly. Rename mapping applies once on the client.
Sources in repository (snapshot 2026-09-29):
examples/remote_inference/omx_act_lan.yaml
remote_inference_docs/hardware_experiment_workbook.md
src/lerobot/rollout/remote_context.py:60

## Slide 5
Two loops share an action buffer
05
Control loop
Read robot
Latest observation
Dispatch next target
Background worker
Request + infer
Accept + merge
Action buffer
30 policy actions at 30 Hz cover 1 second of motion.
Notes: The control loop samples the robot, updates the latest observation and dispatches eligible targets without waiting for a network round trip. At a policy boundary the engine anchors the observation before the next endpoint pop. A background worker requests inference and merges a result. One outstanding action request is allowed. The next motor tick may consume an old eligible target while a newer prediction is in flight. The action buffer bridges timing differences, but active exhaustion is a fault after motion has begun. Thirty actions at a 30-Hz policy rate cover one second. Interpolation adds motor targets between policy endpoints without extending this policy horizon.
Sources in repository (snapshot 2026-09-29):
src/lerobot/rollout/strategies/base.py:61
src/lerobot/rollout/strategies/core.py:166
src/lerobot/rollout/inference/remote.py:338
src/lerobot/inference/execution.py:436
Check your understanding: If inference takes 90 ms, must the motor loop stop for those 90 ms?
Answer: No, while eligible actions remain. It continues dispatching locally. If active playback runs out, the client faults and holds.

## Slide 6
Four decisions shape the motion
06
Request timing
When do we ask for another plan?
Alignment
Which predicted steps are still eligible?
Blending
How do overlapping targets combine?
RTC conditioning
Does inference use the ongoing trajectory?
Each decision can affect task performance. A fresher target is not necessarily a better target.
Notes: Scheduling chooses when to request. Alignment maps an incoming chunk to the client action cursor and removes already committed steps. Blending combines eligible predictions for the same future step. RTC conditions inference on the continuation that will execute during inference. Our first aligned extension coupled alignment to frequent requests. The planned correction separates those concepts using the existing refill setting. Plain alignment/blending is not RTC and is not ACT native temporal ensembling. RTC guided/trained requires explicit supported policy and deployment modes.
Sources in repository (snapshot 2026-09-29):
src/lerobot/inference/execution.py:191
src/lerobot/inference/execution.py:377
src/lerobot/inference/policy_runner.py:217
remote_inference_docs/async_proposal.md:242

## Slide 7
Append preserves the remaining plan
07
Old future
O1
O2
O3
Incoming
N1
N2
N3
N4
N5
After acceptance
O1
O2
O3
N1
N2
N3
N4
N5
The next prediction can wait behind old motion before its first target reaches the robot.
Notes: Illustrative queue diagram. O means a remaining old target and N means a target from the incoming prediction. Append retains old uncommitted actions and puts the new execution slice after them. It does not trim the plain incoming chunk to the current action cursor. Inference can overlap playback, but the new prediction waits behind the old remainder. Early prefetch can therefore produce a seam when a prediction based on an earlier observation starts later. Append limits accepted successors so old predictions do not accumulate into a long chain. The baseline ACT task worked with this behavior and refill 0.1.
Sources in repository (snapshot 2026-09-29):
src/lerobot/inference/execution.py:191
src/lerobot/inference/execution.py:254
src/lerobot/policies/rtc/action_queue.py

## Slide 8
Alignment removes committed steps
08
Prediction at capture
101
102
103
104
105
106
107
108
At acceptance
101
102
103
104
105
106
107
108
Already committed
Eligible future
Cursor progress decides the cut.
Committed means handed to execution. It does not mean physically reached.
Notes: Illustrative human-numbered endpoints. At capture the client has committed 100 actions, so the new prediction starts at endpoint 101. By acceptance, it has committed endpoints 101–103. The incoming prefix for those three endpoints is no longer eligible. The runtime keeps incoming endpoints 104–108 and replaces the uncommitted future. Actual cursor progress drives trimming, including progress between sampling and submission. Request IDs and sequence numbers serve different purposes. No server/client clock comparison is needed. A popped endpoint counts as committed even if interpolation or the hardware has not reached it yet. Physical-state agreement is not guaranteed by index alignment.
Sources in repository (snapshot 2026-09-29):
src/lerobot/inference/execution.py:143
src/lerobot/inference/execution.py:377
Check your understanding: If capture anchors the next action at 101 and the client commits through 103, where does the usable prediction start?
Answer: At 104. The client trims 101–103 using its own cursor. That does not prove the robot physically reached endpoint 103.

## Slide 9
Blending averages matching future targets
09
Old target
40
Incoming target
50
Blended target
45
0.5 × old + 0.5 × incoming
Same future step
Your test: 5 future steps, arm joints only. The gripper follows the incoming prediction.
Notes: Illustrative scalar values in a declared canonical coordinate. For one eligible future step, old=40, incoming=50 and incoming weight=0.5 give a target of 45. The runtime applies this only to explicit permitted continuous components and up to blend_steps matching future steps. Outside that window it uses the incoming prediction. Non-blended components, including the excluded gripper in our test, also follow the incoming prediction. Context and freshness must match. Provenance conservatively keeps the oldest contributing capture time. Repeated overlap can accumulate contributors and change responsiveness. The blend does not change when another request is made.
Sources in repository (snapshot 2026-09-29):
src/lerobot/inference/execution.py:344
src/lerobot/inference/execution.py:377
src/lerobot/remote_inference/chunk_contract.py

## Slide 10
Refill controls when another request starts
10
Remaining playback
1.0 s
0.5 s
0.1 s
More plan remains
Earlier request
with refill 0.5
Later request
with refill 0.1*
*The measured latency floor can trigger earlier. Current aligned mode bypasses this gate.
Notes: The queue contains seconds of future policy playback. Append and RTC use effective_refill=max(configured refill, recent maximum steady-state turnaround + one policy interval). The current aligned implementation bypasses this trigger; the documented correction will apply it to aligned mode too. A larger threshold typically makes requests earlier with more old motion remaining. A smaller threshold lets the plan run longer but offers less turnaround headroom. Interpolation does not extend playback coverage. A threshold near the usable horizon can still request frequently. Increasing action_timeout cannot manufacture actions when a buffer is empty.
Sources in repository (snapshot 2026-09-29):
src/lerobot/inference/execution.py:134
src/lerobot/inference/execution.py:191
remote_inference_docs/async_proposal.md:228
Check your understanding: Today, will changing refill_seconds slow down aligned requests?
Answer: No. The current aligned scheduler ignores the playback trigger. Applying the existing refill mechanism to aligned mode is the next planned correction.

## Slide 11
Parameters worth recognizing first
11
refill_seconds
Request timing and inference headroom
blend_steps / blend_weight
Overlap length and incoming contribution
max_observation_age_s
Maximum permitted action-source age
action_timeout_s
How long a pending request may take
fps /
interpolation_multiplier
Policy pace and intermediate motor targets
Bounds protect execution. Increasing them does not correct stale plans or poor task behavior.
Notes: RemoteInferenceConfig defaults: mode chunk, chunk_merge append, refill_seconds 0.5, blend_steps 0, blend_weight 0.5, max_observation_age_s 2, handshake_timeout_s 10, action_timeout_s 5, language_timeout_s 60 and startup_timeout_s 10. The experiment explicitly used max_observation_age_s 3 and append refill 0.1. These are bounds and configuration defaults, not universal tuning optima. action_fps is deployment-owned and the client fps must match the negotiated policy interval. interpolation_multiplier inserts motor targets between policy endpoints without adding policy coverage. Raw encoding is the default; JPEG is available but quality/latency validation remains separate. Semantics, component names and position hold are correctness contracts rather than tuning knobs.
Sources in repository (snapshot 2026-09-29):
src/lerobot/rollout/inference/factory.py:86
examples/remote_inference/omx_act_lan.yaml
src/lerobot/rollout/remote_context.py:127

## Slide 12
ACT switched prediction after almost every action
12
Actions before switching prediction
Median from client first-dispatch events
Chart: 
| Append | Aligned | Aligned + blend
Actions | 30 | 1 | 1
Baseline
Task completed
Residual bumps
Aligned modes
Worse task progress
About 36 ms between requests
The comparison changed request timing as well as merge behavior.
Notes: Measured from the supplied client logs, grouped by session. Median actions between chunk first-dispatch events: append 30, alignment 1, alignment+blending 1. Median request spacing: 1.009 seconds, 0.036 seconds and 0.036 seconds. All recorded results were accepted, with no reported exhaustion/freshness fault. The retained alignment client log is the second attempt. The first is a separate server-only session, not duplicated requests. Baseline completed the task with bumps. Both aligned modes performed significantly worse. Frequent replacement harming trajectory follow-through is a hypothesis supported by the cadence change, not a proven root cause. This chart summarizes chunk switching, not every individual motor command.
Sources in repository (snapshot 2026-09-29):
test1-client.log
test2-client.log
test3-client.log
server.log
remote_inference_docs/implementation_progress.md

## Slide 13
The timing correction is still planned
13
Implemented today
Fresh advanced observation
+ free worker
Request again
Planned correction
Fresh eligible observation
+ free worker
+ playback below threshold
Request another chunk
Alignment still trims committed steps. Blending still controls matching targets only.
Notes: The current implementation allows aligned inference whenever the worker is free and a fresh advanced observation exists. The revised proposal adds the existing effective-refill playback threshold, with startup/task/control exceptions. It preserves the same alignment and blending rules. No additional minimum-step parameter, automatic tuning or protocol capability is planned solely for this local scheduling change. First proposed hardware check: same ACT checkpoint, blend disabled, refill 0.5 for the logged one-second horizon. This is an initial test point, not a new default or validated optimum. A blend comparison follows only if task performance recovers. Append, RTC and synchronous behavior remain unchanged.
Sources in repository (snapshot 2026-09-29):
src/lerobot/inference/execution.py:191
remote_inference_docs/async_proposal.md:608
remote_inference_docs/implementation_progress.md

## Slide 14
The code follows the process boundary
14
Robot process
Server process
Rollout + motor dispatch
RemoteInferenceEngine + ChunkRuntime
RemoteClient
PolicyServer + SessionWorker
PolicyRunner
Preprocess / model / postprocess
Zenoh + codec
The client owns motion permission. The server owns model and policy-processor state.
Notes: Robot-side rollout strategies call the inference engine and dispatch through robot processors/interpolation. RemoteInferenceEngine owns the latest observation, background request loop, planned holds and event reporting. ChunkRuntime owns scheduling, acceptance, cursor-driven merges and dispatch eligibility. RemoteClient owns contract admission and request/reply exchange. Zenoh transport and the bounded codec carry messages. PolicyServer routes them to a serialized SessionWorker. PolicyRunner applies policy preprocessing, predict_action_chunk and canonical postprocessing. The server process owns model loading, warmup and reset. This separation makes it possible to improve scheduling without rewriting transport or policy integration.
Sources in repository (snapshot 2026-09-29):
src/lerobot/rollout/strategies/core.py
src/lerobot/rollout/inference/remote.py
src/lerobot/inference/execution.py
src/lerobot/remote_inference/client.py
src/lerobot/remote_inference/server.py
src/lerobot/inference/policy_runner.py
src/lerobot/transport/zenoh.py

## Slide 15
One observation through the code
15
1
notify_observation()
Map and anchor
2
runtime.begin()
Reserve one request
3
client.infer()
Send and await reply
4
runner.predict()
Prepare and predict
5
runtime.accept()
Validate and merge
6
send_next_action()
Pop and dispatch
Client worker: 2, 3, 5. Server worker: 4. Control thread: observation and motor dispatch.
Notes: 1. BaseStrategy.run reads the robot and _process_observation_and_notify forwards a policy-boundary sample. 2. RemoteInferenceEngine.notify_observation builds the feature frame, maps names once and anchors aligned observations. 3. The worker calls ChunkRuntime.begin and RemoteClient.infer. 4. SessionWorker._execute invokes PolicyRunner.predict: preprocess, predict_action_chunk, postprocess. 5. RemoteClient validates the response and the engine calls runtime.accept under the task-version lock. 6. The control thread calls engine.get_action, which pops an eligible endpoint. send_next_action applies interpolation and robot action processing, checking dispatch permission before sending. Network work never runs inside the motor-dispatch call.
Sources in repository (snapshot 2026-09-29):
src/lerobot/rollout/strategies/base.py:61
src/lerobot/rollout/inference/remote.py:209
src/lerobot/rollout/inference/remote.py:338
src/lerobot/remote_inference/client.py:370
src/lerobot/remote_inference/server.py:421
src/lerobot/inference/policy_runner.py:217
src/lerobot/inference/execution.py:254
src/lerobot/rollout/strategies/core.py:403

## Slide 16
A reply must belong to the current execution
16
Instance + session
Which server process and robot session?
Request + generation + task
Does this result still belong to this work?
Action cursor
Which endpoints are already committed?
Local capture time
Is the contributing observation too old?
Protocol and capability checks gate compatibility. Build stamps help explain differences.
Notes: A reply carries and is checked against deployment artifact, server instance, session, generation and request context. A task version can make an otherwise well-formed in-flight result obsolete. Data sequence numbers protect ordering and duplicate handling. The action cursor counts committed endpoints and supports alignment; it is distinct from request sequence. The client uses local monotonic observation capture time for age checks. Servers report durations, not authoritative remote clock instants for action alignment. The age is the client acquisition timestamp and does not independently establish camera exposure freshness. Build version/revision logs aid diagnosis, while protocol and required execution capabilities enforce compatibility rather than exact package-version equality.
Sources in repository (snapshot 2026-09-29):
src/lerobot/remote_inference/protocol.py
src/lerobot/remote_inference/client.py:170
src/lerobot/remote_inference/client.py:437
src/lerobot/inference/execution.py:254
src/lerobot/remote_inference/build_info.py

## Slide 17
Faults and reconnection have different jobs
17
Motion failure
Deadline / age / exhaustion
Invalidate motion + hold
Absent client
30 s grace from detection
Ordered cleanup
New session becomes possible
Client death prevents software hold. Cleanup can wait longer for unfinished model work.
Notes: If active playback exhausts, a request deadline expires or an action source becomes too old, ChunkRuntime latches a fault and invalidates motion. The remote engine requests shutdown, and supported position hold is applied through the local control path. Fault teardown suppresses the normal return-to-initial-position behavior. Software hold requires the client process to remain alive. Separately, SessionWorker releases cleanly closed sessions after ordered worker cleanup. An absent client starts a 30-second grace from detected absence, then cleanup proceeds behind unfinished work. A present paused client keeps ownership. A hung worker does not permit another session to take over. A replacement client opens a new session; none of this automatically resumes a faulted rollout. The supplied logs demonstrate clean reuse, not completion of the hardware crash/server-loss tests.
Sources in repository (snapshot 2026-09-29):
src/lerobot/inference/execution.py:172
src/lerobot/rollout/inference/remote.py:123
src/lerobot/rollout/strategies/core.py:222
src/lerobot/remote_inference/server.py:593
Check your understanding: Does restarting the server automatically make a faulted robot resume?
Answer: No. A fault revokes motion permission. A later connection establishes a new session and requires a new operator-authorized run.

## Slide 18
Language requests use a planned hold
18
Query intent
Hold acknowledged
Text inference
Fresh action
Old motion loses eligibility before the query runs.
Healthy active runs can resume after a planned hold.
Implemented with automated coverage. Real language-model acceptance is still pending.
Notes: A text-capable policy and enabled deployment are required. When a query or autosteering request is queued, the engine invalidates old motion and requests a planned hold. The control thread acknowledges hold before the worker serves the query using a fresh held observation and appropriate isolated language processors. After a valid result, a healthy active run requests a fresh post-query action observation and resumes with a usable chunk. Pause, reset, task changes and cancellation must invalidate obsolete results. Autosteering waits for actual action dispatch after a subtask before advancing again. This path has automated coverage but real text-capable checkpoint acceptance remains open. ACT in this demonstration is action-only.
Sources in repository (snapshot 2026-09-29):
src/lerobot/rollout/inference/remote.py:182
src/lerobot/rollout/inference/remote.py:246
src/lerobot/rollout/inference/remote.py:338
src/lerobot/inference/policy_runner.py:322
remote_inference_docs/implementation_progress.md

## Slide 19
A short route through the repository
19
1
Settings
rollout/inference/factory.py
2
Scheduling and merging
inference/execution.py
3
Background loop
rollout/inference/remote.py
4
Network boundary
remote_inference/client.py + server.py
5
Model and motors
inference/policy_runner.py
rollout/strategies/core.py
Paths start under src/lerobot. Notes contain exact entry points and source links.
Notes: Read in this order with the relevant slides open. Start at rollout/inference/factory.py for RemoteInferenceConfig. Then read inference/execution.py: should_request, begin, accept, _accept_aligned, pop. Then rollout/inference/remote.py: notify_observation and _loop. Follow remote_inference/client.py infer to remote_inference/server.py SessionWorker._execute and inference/policy_runner.py predict. Finally inspect rollout/strategies/core.py send_next_action. Contracts live in inference/contracts.py. Protocol, codec and Zenoh transport explain boundaries when needed. The authoritative proposal describes the planned timing correction, while the current execution code still implements the old trigger. implementation_progress.md records what was actually tested.
Sources in repository (snapshot 2026-09-29):
src/lerobot/rollout/inference/factory.py:86
src/lerobot/inference/execution.py:191
src/lerobot/rollout/inference/remote.py:338
src/lerobot/remote_inference/client.py:370
src/lerobot/remote_inference/server.py:421
src/lerobot/inference/policy_runner.py:217
src/lerobot/rollout/strategies/core.py:403

## Slide 20
Three questions to check your mental model
20
1
Who decides whether the next target
may reach the motors?
2
Why can correctly aligned actions
still produce a worse task result?
3
What changes in the next implementation
and what stays the same?
Answers are in the notes. The browser version lets you reveal them when ready.
Notes: Answers: 1. The client owns motion permission through the runtime and control loop. A correctly delivered server response still needs validation and eligibility checks. 2. Alignment decides which future indices remain valid. Rapidly replacing plans can change the learned behavior, and actual hardware state can differ from the predicted trajectory. 3. The next change adds the existing playback/refill gate to aligned requests. It leaves alignment, blending and fault guarantees intact and does not add a new cadence knob. Read the proposal for intent and the progress document for implemented/tested status. The remaining real language/lifecycle gates remain open.
Sources in repository (snapshot 2026-09-29):
remote_inference_docs/async_proposal.md
remote_inference_docs/implementation_progress.md
Check your understanding: Who permits motion, why can correct alignment hurt a task, and what changes next?
Answer: The client permits motion. Correct temporal alignment can still replace a useful trajectory too frequently. The planned change adds buffer-driven request timing to aligned mode, while keeping its merge and fault rules.